## Slide 1: An Equation-free Based Coupling Approach for Long-term Cryogenic Tank Behavior Predictions Qiyun Cheng, Shanbin Shi, and Wei Ji | Rensselaer Polytechnic Institute Mamoru Ishii | Purdue University Michael Harris | NASA Kennedy Space Center
Presented By Qiyun Cheng
Advisor: Dr. Wei Ji
Thermal & Fluids Analysis Workshop TFAWS 2022 September 6th-9th, 2022
Virtual Conference
TFAWS Cryothermal Paper Session

## Slide 2: Contents
Background
Technic Approach
  Equation-free Modeling
  Equation-free Based Coupling Approach
Research Objectives
Equation-free Based Coupling Approach Applications
  Pipe Flow with Periodical Pressure Boundary
  Cryogenic Tank Self-pressurization
Conclusions

## Slide 3: Background
Cryogenic storage tank used in NASA’s space missions
  Propellant & life support consumables
Heat leaks from surroundings lead to excessive tank pressures
  Self-pressurization process
Cryogenic storage tank management
  Active cooling method (jet injection)
Periodical behaviors
  Similar heating-depressurization cycles
  Disturbed initial/boundary conditions
E. Ramos, Ph. D. dissertation, Georgia Institute of Technology, May 2021

## Slide 4: Background (Cont’d)
Complex phenomenon in microgravity environment
  Thermal stratification
  Natural convection
Need fast and accurate numerical tools for long-term tank behavior predictions
  High fidelity CFD simulation is computational expensive
  Fast nodal code simulation lacks fine-scale details inside the lumps
    All parameters are the same in one lump, no distribution
    Flow patterns inside the lump affect heat transfer
Coupled method is desired to take advantages of both approaches

## Slide 5: Technic Approach
Equation-free Modeling
  Object:
    Use the microscopic simulator to obtain the macroscopic solutions with reasonable computational consumption
  Assumptions:
    An accurate microscopic simulator exists
    Macroscopic governing equations are unavailable
    The macroscopic phenomenon is more important

## Slide 6: Technic Approach (Cont’d)
Equation-free Modeling
  Macroscopic time steper:
    Given the macroscopic initial condition at time , create the corresponding microscopic initial condition .
    Run microscopic simulator over a short interval to obtain (t).
    Construct the macroscopic evolution of based on the microscopic results.
    Extrapolate the macroscopic results to .
I.G. Kevrekidis, G. Samaey,"Equation-free multiscale computation: algorithms and applications", Annual Review of Physical Chemistry, 60: 321–344 (2009).
S. Sirisup, et al. "Equation-free/Galerkin-free POD-assisted computation of incompressible flows." Journal of Computational Physics 207.2: 568-587 (2005).

## Slide 7: Technic Approach (Cont’d)
Equation-free Based Coupling Approach
  Adapt the equation-free modeling idea to coupling approach
Macroscopic simulator
Nodal Code
Microscopic simulator
CFD Code
Construct and extrapolate
Corrections
Equation-free Modeling
Equation-free Based Coupling
Doesn’t exist
Run for the whole problem
Use in each time step
Run for a short period

## Slide 8: Technic Approach (Cont’d)
Equation-free Based Coupling Approach
  Assume the CFD model is accurate
  Derive the conversion equation between the two codes is impossible
  Adapt the equation-free idea to find the conversion correlations
CFD code governing equation (Volume Averaged Result):
Nodal code governing equation:
Equation-free corrections

## Slide 9: Technic Approach (Cont’d)
Equation-free Based Coupling Approach
  Periodical behavior of cryogenic tanks
    Co-solve for the first cycle to get the equation-free corrections
    Use the nodal code for the rest of similar cycles with corrections
  Corrections are obtained through the on-the-fly co-solve process
  Expect better performance by introducing Nodal code solutions
  No 1D/3D data transfer error

## Slide 10: Research Objectives
Efficient use of the CFD and nodal tools based on the equation-free based coupling approach.
  Fit the data within the first cycle (Co-solving period)
  Extrapolate the corrections to the whole problem (disturbed conditions)

## Slide 11: Equation-free Based Coupling Approach Applications
Pipe Flow with Periodical Pressure Boundary
  Internal laminar flow of a straight, circular pipe
  Change the inlet pressure to mimic the heating-depressurization cycle
Liquid: Water
Pipe length = 1 m
Inner diameter = 0.01 m
Laminar flow: 0 < Re < 2,000
P inlet
P outlet = 0

## Slide 12: Equation-free Based Coupling Approach Applications
Pipe Flow with Periodical Pressure Boundary
  Results of the first cycle
Nodal code
CFD code
Equation-free Based Approach
Y = Nodal(t) * 0.8362 + 0.006732
Difference from the hydrodynamic entrance effect

## Slide 13: Equation-free Based Coupling Approach Applications
Pipe Flow with Periodical Pressure Boundary
  Equation-free based coupling results
Nodal code
CFD code
Equation-free Modeling
Y = Nodal(t) * 0.8362 + 0.006732

## Slide 14: Equation-free Based Coupling Approach Applications
Pipe Flow with Periodical Pressure Boundary
  The correlation can correct the hydrodynamic entrance effect in that geometry within a range of fluid parameter changes.
  Reynold number goes slightly beyond the laminar region.
…
CFD result at time
Nodal result at time
CFD result at time , position r
Nodal result at time , position r
…

## Slide 15: Equation-free Based Coupling Approach Applications
Cryogenic Tank Self-pressurization
Heat Flux
R=0.5m
H=1m
    Liquid and vapor nitrogen, 75% filling level
    Initial pressure: 100kPa
    Initial temperature: 77.24K (uniform, saturated)
    Adiabatic side and bottom walls
    No inlet and outlet, the tank is pressurized
    Constant heat flux from the lid.
Adiabatic wall
    Case1: heat flux = 50 W/m^2, flow time = 100s
    Case2: heat flux = 80 W/m^2, flow time = 200s

## Slide 16: Equation-free Based Coupling Approach Applications
Volume Averaged Temperature Results Comparison (Heat Flux = )
Vapor
Liquid
1
2
3
4
5

## Slide 17: Equation-free Based Coupling Approach Applications
Equation-free Corrections
  Linear regression
  Phase diagram of SF1-CFD1

## Slide 18: Equation-free Based Coupling Approach Applications
Corrected Results Comparison of Heat Flux =

## Slide 19: Equation-free Based Coupling Approach Applications
Extrapolate to Heat Flux =

## Slide 20: Conclusions
Equation-free based coupling approach
  Capable to correct the nodal code results with disturbed conditions
  Easy to apply and computational efficient
  No 1D/3D data transfer error
Planned activity
  Use equation-free coupling approach to tanks with heat-depressurization cycles
  Validate the coupling approach with experiment data

## Slide 21: Acknowledgement
This work was supported by an Early-Stage Innovations Grant through the NASA’s Space Technology Research Grants Program under Grant 80NSSC20K0303.
The authors would like to thank C&R Technologies (CRTech) for providing the computational software SINDA/FLUINT & Thermal Desktop for this research.

## Slide 22
Thank You
and
Questions?
For further details contact:
Qiyun Cheng
chengq3@rpi.edu