## Slide 1: Accelerating Steady-State Convergence of Compressible Flow Simulations via Nonlinear Elimination Kyle Thompson, Matthew O’Connell, and Cameron Druyor NASA Langley Research Center
Presented By Kyle Thompson
Thermal & Fluids Analysis Workshop TFAWS 2022 September 6th-9th, 2022
Virtual Conference
TFAWS Aerothermal Paper Session

## Slide 2: Motivation
What is required is an automated capability that delivers hands-off solid convergence under all reasonable anticipated flow conditions with a high tolerance to mesh irregularities and small-scale unsteadiness.
- CFD 2030 Vision Study

## Slide 3: Motivation
Progress has been made in the last two decades toward robust nonlinear solver technology
  Multigrid methods
  Constraint-based solver techniques
  Newton-Krylov techniques
Newton-Krylov solvers can accelerate iterative converge under certain conditions
  Fast quadratic convergence with ”good” initial conditions
  These solvers can stagnate when strong nonlinearities are present in the flow field
  Strong bow shocks in hypersonic flow can lead to wasteful nonlinear iterations early in the simulation

## Slide 4: Newton-Krylov Efficiency
Problem: Newton-Krylov solver iterations are expensive compared to other nonlinear solver techniques.
  Each iteration requires solving an ill-conditioned linear system, that is expensive to construct and robustly solve.
  If quadratic convergence is achieved quickly, then this is not a problem. Otherwise, the efficiency of the solver deteriorates.
Solution: use a robust and efficient globalization strategy.
  Many techniques are studied in the literature
  Pseudo-transient continuation, line search, and trust region methods are popular
  Most focus on “hill-climbing” methods, but simple methods fail when shocks are present

## Slide 5: Inefficiency of Newton-Krylov with Shocks
When strong shocks are present, Newton-Krylov methods stagnate early on and then rapidly converge after many nonlinear iterations
  All progress is stymied by the shock until it settles into the final location
  Using a Newton-Krylov method is inefficient here, because a small region (the shock) is holding up progress everywhere else
Expensive/wasteful iterations while shock is moving
Fast quadratic convergence
Solution evolves slowly from impulse freestream condition
Example: Cylinder in Hypersonic Flow

## Slide 6: Nonlinear Elimination
The failure of Newton-Krylov solvers when nonlinearities are unbalanced is a known problem
  Nonlinear preconditioners can be used to mitigate unbalanced nonlinearities
Nonlinear Elimination
  Developed by Cai and Li1
  Partition regions with strong nonlinearity and solve local subproblem
  Solving smaller, better-conditioned subproblems provides a better starting solution for the global ill-conditioned problem
Cylinder Flow Flux Balance
Large flux imbalance at shock
Flux relatively balanced elsewhere
1X.-C. Cai and X. Li, Inexact Newton methods with restricted additive Schwarz based nonlinear elimination for problems with high local nonlinearity, SIAM J. Sci. Comput., 33 (2011), pp.746-762.

## Slide 7: Identifying Imbalanced Nonlinearities
A shock sensor is used to identify the ”bad” region of high nonlinearity
  Lovely and Haimes1 sensor filtered by Gnoffo and White2 pressure-based limiter function is used to identify the strong shock iso-surface
In practice, any value > ~0.1 indicates the vicinity of a shock
Apply shock sensor
Shock region
1Lovely D, H. R., Shock detection from computational fluid dynamics results, AIAA Paper 1999-3285
2Gnoffo, P., and White, J. A., Computational Aerothermodynamic Simulation Issues on Unstructured Grids, AIAA Paper 2004-2371

## Slide 8: Nonlinear Elimination: Shock Subdomain Solve
Subdomain partitioning via shock sensor
  Solve subdomain and keep solution in shock (red) region
  Discard solved subdomain solution in level 1 (green) and level 2 (blue) overlap regions
Before Subsolve
After Subsolve
Keep solution in shock (red) region
Discard solution in overlap (green/blue) region
Identify Shock Region and Overlap
Subdomain Flux Balance
Solution fixed in outer overlap (blue) region
Flat and smooth is better for fast convergence
Remove region outside of subdomain (grey)

## Slide 9: CFD Flow Solver: HyperSolve
All results shown use HyperSolve
  Developed at NASA Langley Research Center
  Edge-based unstructured finite-volume CFD flow solver
  Dynamic load balancing on shock-detected subdomains
  Jacobian-Free Newton-Krylov (JFNK) nonlinear solver
JFNK solver used on both global and subdomain solves
  HyperSolve-PETSc interface via Enigma library1
  Linear solver: Additive-Schwarz (ILU-0) right-preconditioned GMRES(50)
  Newton globalization via pseudo-transient continuation with backtracking line search
1 K. Thompson, and M. O’Connell, Streamlined Convergence Acceleration for CFD Codes, AIAA 2019-3709

## Slide 10: Case: Cylinder – Quad Mesh
Subdomain Solve Settings | 
Relative Tolerance | 0.1
Solve Frequency | 1
Subdomain Overlap | 2
Max Iterations | 10
Flow Conditions | 
Freestream Density | 0.001 kg/m3
Freestream Speed | 5000 m/s
Freestream Temperature | 200 K
Wall Temperature | 500 K
Using JFNK with nonlinear elimination reduces total simulation time
  Minimal effect of nonlinear elimination once quadratic convergence is achieved
~22% improvement

## Slide 11: Case: Cylinder – Triangle Mesh
JFNK + NE more effective on triangle mesh than shock-adapted quad mesh
  Likely due to increased dissipation due to shock misalignment
~38% improvement
Subdomain Solve Settings | 
Relative Tolerance | 0.1
Solve Frequency | 1
Subdomain Overlap | 2
Max Iterations | 10
Flow Conditions | 
Freestream Density | 0.001 kg/m3
Freestream Speed | 5000 m/s
Freestream Temperature | 200 K
Wall Temperature | 500 K

## Slide 12: Case: Hemisphere – Hexahedral Mesh
Subdomain solve efficiency sensitive to solve frequency
  Increasing the frequency increases simulation time more than decreasing iteration count
~20% improvement
Subdomain Solve Settings | 
Relative Tolerance | 0.1
Solve Frequency | 5
Subdomain Overlap | 2
Max Iterations | 10
Flow Conditions | 
Freestream Density | 0.01 kg/m3
Freestream Speed | 1000 m/s
Freestream Temperature | 200 K
Wall Temperature | 500 K

## Slide 13: Case: Hemisphere – Tetrahedral Mesh
JFNK + NE more effective and parameter-agnostic on tetrahedral mesh than shock-aligned hexahedral mesh
  Likely for same reasons as triangle vs quad mesh convergence
~25% improvement
Subdomain Solve Settings | 
Relative Tolerance | 0.1
Solve Frequency | 1
Subdomain Overlap | 2
Max Iterations | 10
Flow Conditions | 
Freestream Density | 0.01 kg/m3
Freestream Speed | 1000 m/s
Freestream Temperature | 200 K
Wall Temperature | 500 K

## Slide 14: Conclusions
Nonlinear elimination can be effectively used to decrease the total time-to-solution for Newton-Krylov nonlinear solvers
  Key ingredients: shock sensor, dynamic load balancing, subdomain solution transfer
  Provides a mechanism for balancing overall nonlinearity of the problem
Efficacy of nonlinear elimination is dependent on the relative imbalance of localized nonlinearities
  If the problem is “globally bad”, then subdomain solves are not cost effective
  Fortunately, bow shocks are typically highly localized phenomena
Effectiveness of shock subdomain solves includes tunable parameters
  Future work to automate these parameters for optimal iterative convergence