## Slide 1: Model Checks: How to Ensure a Model is Working as Intended Kim Martin (NASA Langley) Brian Comber (NASA Goddard)
Thermal & Fluids Analysis Workshop TFAWS 2023 August 21-25, 2023
NASA Goddard Space Flight Center
Greenbelt, MD
TFAWS Technical Course
Notes: Kim

## Slide 2: Course Outline
Basics of Thermal Desktop Model Reviews
Thermal Desktop Model Checklist
Goddard and Langley Model Audit Outputs
Additional Tools
Demos
Notes: Kim

## Slide 3: Basics
Why should you do a model review?
  Independent assessment builds confidence in the model both for the analyst and project
  Another perspective can show longstanding model mistakes and incorrect simplifications
  Even experienced analysts can use a second opinion and outside checks
  Builds model knowledge and capability in early career analysts
When should a model review be done?
  Commonly at Langley, before milestone project reviews like Preliminary Design Review (PDR) and Critical Design Review (CDR)
  Additional reviews could be done as needed (e.g. prior to system-level testing, model delivery, or integration into a higher-level model)
What does a model review encompass?
  All aspects of the model, including base geometry, thermal desktop elements like connectivity/heat sources/model logic, thermal radiation, and results
  Could be done in conjunction with document review (e.g. model reports, project milestone slides)
Notes: Kim

## Slide 4: Basics
Who should perform a model review?
  For simple models with common features, any engineer with exposure to thermal modeling practices
  It can be valuable even for early-career engineers to do model reviews, to gain exposure to model techniques
  For specialized models with unusual features or analysis techniques, it is valuable to select a reviewer familiar with the subject matter
  Best practice is that the reviewer is not an engineer associated with the project
How long should a model review take?
  For many Langley thermal models (electronics boxes, small satellites), two weeks is a standard window to give the reviewer
  For more complicated models, a monthlong window might be more realistic
  Actual labor time is typically ½ day to 2 days
  Larger models, such as full spacecraft, might take months and multiple analysts
  Request a model review as soon as reasonably possible, to ensure time to assign reviewer and complete the review
Notes: Kim

## Slide 5: Basics
What should be delivered for a model review?
  The model, with all relevant files
    Thermophysical and optical property files
    External model logic files
    Any xref files
  Supporting documentation or files (e.g., CAD, review slides)
  Model log or documentation, if used
  Model output template, if used

## Slide 6: Basics
Self reviews vs. peer reviews
  The checks in this document can be used by the original analyst as well
  It is a good practice to self-review a model using some or all of these checks prior to requesting an independent review
Reference documents when doing a review
  NASA Passive Thermal Control Engineering Guidebook
    Cross-center thermal best practices document
  Cross-Program Design Specification for Natural Environments (DSNE)
    General reference document for common space and planetary thermal environments
  Lunar Thermal Analysis Guidebook (LTAG)
    Moon-specific environmental document, with Thermal Desktop modeling guidelines
  This Slide Package
Most common issues found during model reviews
  Units
  Property assignments
  Incorrect logic
  Radiation surface assignment
  Contactor errors
Notes: Kim

## Slide 7: Demo Model
We generated this future NASA concept as a way to show some of these checks in real-time today
We will switch back and forth between a detailed checklist and this model as the course progresses
Model demos denoted by

## Slide 8: Model Units
Check unit preferences in Thermal Desktop
  General standard for NASA is all SI units, but some projects may choose to make exceptions, particularly for lengths
  Caution: check user logic for problems that could arise from changing units
Make note of model units for reviewing:
  Model objects that use symbols
  xrefs
Command: Rcpreferences

## Slide 9: Sanity Check Against CAD
Ideally, Computer Aided Design (CAD) and Thermal Desktop geometry should have the same coordinate system for ease of import
Checker should import CAD and ensure that the thermal geometry reasonably matches.
Check critical dimensions like thicknesses, if necessary
  Determine if the model is using surfaces vs. solids properly
If post-processing data mappers are present in the model, ensure that they align with thermal model
Notes: Kim

## Slide 10: Radiation Analysis Groups
View model by each analysis group (via Model Browser)
  Check for missing or extraneous surfaces
  Zoom Extents is useful to make sure all surfaces are visible on screen
    May not work correctly if xrefs are used
  If symbol-driven assemblies or trackers are used, try changing the symbols to make sure the whole radiation group moves together
  Ensure that there is only one external radiation analysis group and internally-facing surfaces do not use that group
Command: Rcmodelbrowser
Notes: Kim
ENTERPRISE

## Slide 11: Radiation Analysis Groups
Display active sides for each analysis group
  Look for inverted or double-sided surfaces that don’t make physical sense
Command: editActivePrefs
Notes: Kim
ENTERPRISE

## Slide 12: Optical Properties
View model by optical properties
  Property name, absorptivity, emissivity
  Look for unexpected changes in properties on single bodies, or unreasonable values
  Look for surfaces assigned DEFAULT optical properties in the model browser
Command: editPropData
Notes: Kim

## Slide 13: Thermophysical Properties
View model by material properties
  Property name, conductivity, specific heat, density, thickness
  Look for unexpected changes in properties on single bodies, or unreasonable values
  Look for properties assigned DEFAULT material in the model browser
  Be sure to assign unique colors to property names when viewing by name
Command: editThermoPropData
Notes: Kim

## Slide 14: Insulated and Multilayer Insulation (MLI)-Covered Surfaces
View surfaces that have insulation via Model Checks  Display Active Sides  Insulation)
  Ensure insulated surfaces are using insulation-related optical properties
Command: editActivePrefs
Notes: Kim

## Slide 15: Insulated and MLI-Covered Surfaces
Plot surfaces by e* value
Plot surfaces by k* if applicable
Command: RcPlotEStar
RcPlotKStar
Notes: Kim
ENTERPRISE

## Slide 16: Optical Property Database
Verify that all optical properties have properly assigned values
  No placeholder values
  All properties have reliable sources listed, such as published papers or vendor datasheets
Check for duplicate properties with similar names
Check that aliases are set appropriately
Command: editPropData
Notes: Kim

## Slide 17: Thermophysical Property Database
Verify that all material properties have properly assigned values
  No placeholder values
  All properties have reliable sources listed, such as published papers or vendor datasheets
Check for duplicate properties with similar names
Check that temperature-dependent properties have properties over all temperatures predicted for the material
Check that aliases are set appropriately
Command: editThermoPropData
Notes: Kim

## Slide 18: Mesh Density
Turn on surface visibility
Visually check for reasonable mesh density
  Are there sufficient nodes to capture heat paths?
  Are there nodes located where contactors are connecting?
  Are there places where it would be better to merge nodes instead of using high-value conductors?
Plot by skew
  Thermal Desktop will abort the run (if checked in User Preferences: Calculations) if skew is above 0.999
  Address areas of unacceptably high skew by re-meshing if possible
Command:
Rcpreferences
Command:
_RcPlotSkew
Notes: Kim

## Slide 19: Geometry Checks
Overlapping Surfaces
  Writes a log file (CheckOverlappingSurfaces.log) to model directory listing any surfaces overlapping above user-input threshold value
  Tool described later in presentation can help parse the output
Show Free Edges
  Highlights discontinuities in finite elements with a red line
  Shows the outline of a finite element mesh as well, which is normal
Show material orienters for anisotropic solids and surfaces and verify proper assignment and alignment
Command: RcCheckOverlappingSurfaces
RcFreeEdges
Notes: Kim
ENTERPRISE

## Slide 20: Conductors/Contactors
Show all contact/contactor markers
  Verify that the contactor faces are set up in a physically meaningful way
  For a large model, it may be better to do this in batches
Open each contactor via the model browser
  Check contactor values
  Check warning messages
    Via “show calcs” in each contactor and checking the command window output, or run a case and check the ContactorData folder
  Use “Display Only” for the from and to surfaces separately
Best practice is that the “from” surface has larger area than the “to” surface. If this is the case, the contactor will show up as green in the Model Browser.
  Red contactor indicates the “from” surface is larger than the “to” surface
Command: RcShowContactorMarkers
RcShowContactMarkers
Contactor Markers
Notes: Kim

## Slide 21: Mass
Do model mass check
  Select the whole model, or portions, and use the “Calculate Mass” feature
  Is the model close to total mass Current Best Estimate (CBE)?
  Are submodel masses close to submodel mass CBE?
Command: RcCalcMass
Notes: Kim

## Slide 22: Nodes
Check nodes by shape of node
  Sphere: Diffusion or generated by surface
  Cube: Overridden to arithmetic
  Pyramid: Overridden to boundary
Check for arithmetic nodes overridden by surface, use "Generate Nodes Option" by sequence shown in screenshot
  0=material property, 1=arithmetic
Ensure arithmetic nodes or diffusion nodes not associated with surfaces are properly applied
Command: RcPlotGenNodes
Notes: Kim’s

## Slide 23: Nodes
Disposition any duplicate nodes
  In the case set manager, ensure that "prompt if duplicate nodes found" is checked
  Duplicate nodes may be acceptable for merged interfaces, but generally not desirable (merge nodes instead)
    Use "Duplicate Node Exceptions" in case set manager and maintain the warning for the future
Command: RcCaseSet
Notes: Kim

## Slide 24: Conductance/Capacitance
Check multipliers on density and conductivity on surfaces and solids
  A large override may indicate a nonphysical representation
  If using a density override, use conductivity override values to match
Check nodes over-ridden for thermal mass
Create cc file and check for errors
Command: RcPlotDensityMult
RcPlotKuMult
RcPlotKvMult
RcPlotKwMult
Notes: Kim

## Slide 25: Model Connectivity Test
Save as a new model and check internal connectivity
Connect each internally-continuous body to a boundary node, turn off radiation and convection, and run steady state to ensure that all surfaces are connected as intended
  Turning off all heat loads except for one or adding a very high-value heat load can help visualize the heat flow
Notes: Kim

## Slide 26: Heaters and Heat Loads
In the model browser, check each heater and heat load and Thermo-Electric Cooler (TEC)
  Plot surfaces and markers for each heatload, to understand where they are applied
  Verify consistent units (absolute? Per area?)
  Verify enable/disable flags
  Verify thermal heat dissipation is electronics waste heat and not necessarily electronics power
  Check heater performance in .sav or .out to ensure they are working as expected. Print out duty cycles in .us* file.
Notes: Brian

## Slide 27: Symbols
View model by symbols in Model Browser, and ensure that correct symbols are used
  Symbols that are not used may indicate an oversight
Check symbols in symbol manager for consistency
  Does the model follow a symbol naming convention?
    Confusing naming convention could result in duplicate symbols (e.g. flag_op vs. switch_op vs. power_state vs. op_flag)
  Are symbol units clarified in the comment block?
  Are the units identified consistent with the model units? And if not, is the appropriate conversion done when using the symbol?
Symbols that do not have a “+” next to them are never used in the model
Notes: Brian

## Slide 28: Logic
Check logic in enable blocks to ensure logic turns on and off consistently
  Can temporarily manipulate model enable flags to check that logic turns on and off in the correct conditions
  Save a separate version before making any changes like this
Check each logic object (e.g. arrays, PID controllers)
Check unit consistency in logic objects
  This can be particularly hard to catch for time- or temperature-based array interpolations
Check that time-based logic matches the duration of cases
Look for logic in include files
Actually read the cautions that come up in the command line when the model is run
Command: RcLogic
Notes: Brian

## Slide 29: Initial Condition - Temperature
Run a transient case that is not initialized from another case or steady state, and view the temperature at the first timestep
  Is the temperature consistent throughout?
Set the initial temperature symbol to a different value, re-run the case and replot the temperature at the first timestep
  Does this change the initial temperature of all nodes?

## Slide 30: Measures
Ensure that measures are contacting the correct surfaces
Display measures on color plot and make sure they are the correct color
Ensure that measures move with articulators if necessary
Note: this color plot also indicates node density issues

## Slide 31: Orbits
Check orbits for valid parameters
  Solar flux, planetshine, and albedo have sensible min/max values per guiding documents like DSNE
Plot orbits
  Check whether the model seems oriented correctly
Command: RcManageOrbits
RcShowOrbit
Notes: Brian
Enterprise

## Slide 32: Trackers and Assemblies
In the model browser, check assemblies and trackers
  Is it a consistent body, with no surfaces/solids left out?
  Check operation of trackers by viewing model around orbit
Notes: Brian

## Slide 33: Analysis Cases
On the "Calculations" tab:
  Check for reasonable values on:
    A/DRLXCA (default value is 0.001. Some users may increase this to speed up model runs, but a much larger value could result in poor convergence)
    DTIMEI (should be 0 except in exceptional circumstances)
    EBALSA <0.01 and EBALNA < 0.001 for steady state runs
    DTMPCA < 0.1 and ATMPCA < 5
  Check for steady-state versus transient, and sufficient length of transient
    If running steady state for a case with heater, it is best to run a transient run afterward, to allow heaters to cycle to their setpoint
Notes: Brian
A/DRLXCA: temperature-based convergence criteria per iteration
DTIMEI: user-enforced timestep
EBALSA/EBALNA: Energy-based convergence criteria, SS only
DTMPCA/ATMPCA: temperature-based convergence criteria per time step

## Slide 34: Analysis Cases
Check BUILD block
  Verify that case-specific submodels (e.g., Thermal Vacuum (TVAC) configuration, ground support equipment, convection, landed surface, launch are only built in appropriate cases)
Notes: Brian

## Slide 35: Analysis Cases
On the "Props" tab: check thermophysical/ optical property aliases
  If properties have a permanent alias, strongly consider changing the property itself and not using an alias
On the "Symbols" tab: Check symbol overrides
  e.g. Operational cases use op flags and op heater setpoints
  Ensure reasonable number of symbol overrides and no permanent overrides that only exist on Case Set Manager
Note: Goddard best practice is to use separate .tdp and .rco files for Beginning of Life (BOL)/End of Life (EOL) and to deliver models with all property aliases removed
Notes: Brian

## Slide 36: Analysis Cases – radks Settings
Check number of rays reasonable
  Generally, 50k rays at a minimum, and 500k is an all-around "good" number, but it depends on geometry
  Tall, thin structures may need more rays
To check:
  Plot heat rates and look for unexpected heat rate hot spots
  Check that total view factor (Fij) is >0.98
    "Output Area*Fij File" option under the Radiation Calculations submenu, then open the AREAFIJ.XLS file to examine Fij values
  Can also double the number of rays and ensure that the results do not change
Command: outputAreaFij
Notes: Brian

## Slide 37: Analysis Cases – radks Settings
Model checker should view radiation analysis groups by temperature
For radiation groups with large differences in temperature, ensure that the energy is well book-kept, not just the view factors
  Small view factors can be a majority of the energy in some cases
Set Bij/Fij Cutoff factor low AND output Bij very high for such radiation groups
Be aware of cases with low emissivity and high temperature range (i.e., sun shields) that may need additional consideration for non-grey behavior
Notes: Brian

## Slide 38: Analysis Cases – radks Settings
Verify space node temperature
  If set with a symbol, check whether it is changed in case symbol overrides
  Double check after loading .sav file by creating a node and naming it SPACE.1 and read temperature
Check radks to space setting
  Disabled for internal groups?
  Enabled for groups with view to space?
Notes: Brian

## Slide 39: Analysis Cases – radks Settings
Check that the correct orbit is selected for the case name
Ideally, verify that radks output files have user-identifiable names (not auto-generated)
Check correct spectrum used
  This is a setting not often used for purely space-based analysis, but in thermal testing where lamps are used
Check oct tree settings
  Thermal: Radiation Calculations: Optimize Cells will provide optimum settings for the particular model
  Usually, 13 oct tree subdivisions and 8 max surfaces per cell
Notes: Brian

## Slide 40: Analysis Cases – radks Settings
Verify articulating radks used where necessary
  Important for systems with parts that will move during a case
Verify that an appropriate percent of radks are being printed
  Especially for models with big temperature differences, sometimes small views can be a lot of heat
Notes: Brian

## Slide 41: Results
Run a few cases to make sure they run
  Ask originating analyst which cases are most applicable
  Check all warning and caution messages (including cautions about symbol unit mismatch)
  Check for balanced heat in/out
View thermal results on the model, looking for:
  Large gradients
  Sudden temperature changes
  Unreasonable min/max values
View absorbed solar/planetary flux on model
Notes: Brian

## Slide 42: Debugging Slow Models
If a model is running slowly, calculating minimum thermal time constant (CSGMIN) can identify why
  Enable outputting capacitance and conductors on the .sav file and run the case
  In the model browser, enable CSG output
  Smaller CSG values indicate low mass/high conductivity nodes
  Additional tools include CALL SETTL and PRINTTL, which will report which nodes are limiting for each timestep
  Improvement options include:
    Increasing mesh density
    Changing to arithmetic nodes (if applicable)
    Decreasing artificially high contactor/conductor values used for internal contact
    Merging nodes instead of using contactors/conductors for internal contact
Notes: Brian
Enterprise?

## Slide 43: Best Practices
While not affecting model accuracy, these best practices can help avoid confusion and mistakes, and speed up model reviews
  No unused optical or thermophysical properties in model after delivery
  No duplicate properties (i.e., multiple aluminum 6061 T6's) unless controlled by different organizations
  No thermal entities (heat loads, heaters, etc.) allowed to be disabled in model delivery
  Inactive surfaces only used as blockers need to be in their own submodel called INACTIVE
  Verify Software version is latest/project required
  Check consistent MLI nodal offsets
  Symbols grouped by tabs
  Avoid nesting assemblies
  Check for good naming convention for submodels (usually using prefixes)
  Use layers in a way that avoids confusion among your group members
    For example, model is on one layer and organized by submodels, but CAD surfaces are on other layers
    Do not allow important model details to hide in obscure layers.
  When a model is intended to be xref'd, use a consistent prefix to keep track of which symbols and submodels belong to which models
  Steady state heaters set to damped proportional control
  Contactors, conductors, heat loads, heaters, surfaces/solids should have descriptive comments
  Contactors should use ray trace algorithm, if possible, for face connections
  Heat Loads, heaters, conductors, contactors, etc., are defined in the same submodel as the nodes on which they are applied
  Sensor and thermostat locations should be modeled as measurement points to keep node numbers down. Put them in a unique submodel
  Property values should include reference/source
  Avoid include files if possible – put user defined logic in Logic Manager
  No use of symmetry as a model reduction tactic in subsystem or system level models
  Use a consistent naming convention for symbols (Langley uses Hungarian notation)
    The names of all symbols are prefaced by type, and the prefixes are standardized
    Can also include units as a suffix. e.g. T_initial_shuttle_C (initial temperature of the shuttle, in °C), or Qflx_torpedo_W_m2 (heat flux of a photon torpedo, in W/m^2)
Notes: Brian

## Slide 44: Useful Tools
A few useful tools were developed at Goddard to make it easier for the model reviewer to survey the entire model very quickly for a select few common model issues that can be very time-intensive to find
Surface Consistency Check
  Uses the "output to TSS" feature in Thermal Desktop and Excel VBA to read that output
  Lists all surfaces and flags any that seem to need MLI properties and do not have them or have effective emissivity without a proper outer layer property
  Lists all optical properties that appear for a particular thermophysical property to ensure that no unrealistic pairings appear (ex: tiodize on aluminum or the presence of the "DEFAULT" property)
Mass and Conductivity Multiplier Finder
  Somewhat made obsolete by "color by" feature in TD for multipliers, but can show at a glance if large multipliers are used to fix model mass so that reviewer can check for accuracy.
Conductance Reader
  List all conductors and check for very large conductances that can make the model run slowly
Overlapping Surfaces Clean-Up
  Reads the checkoverlappingsurfaces output from Thermal Desktop and sorts by percentage. It cleans up the many duplicates that currently (2020) exist in the TD output
  Flags the T^4 ratio of the two surface temperatures to highlight small overlaps that might be below a model audit threshold (say, 10%), but could be so different in temperature that they should be fixed (i.e., a warm object sticking through a cold one).
FilePlottingTools v3.1 (Langley)
Notes: Brian

## Slide 45: Surface Consistency Check Output
Shows each thermophysical property and the various optical properties that pair with it. Manually review and highlight pairs that merit further review by the modeler. Example: A titanium part that has an Invar optical property, or any use of the DEFAULT property, which we discourage
Button jumps to an example of the selected pairing in the full list
In full list, highlights any line that has a listed property associated with MLI, but no "MLI-ish" nodalization. This will mostly result in flagging single layer soft structure, but it is a nice sanity check.
In full list, highlights any line that has "MLI-ish" numbering (user inputs what a typical difference between surface and MLI node would be) but lacks an MLI outer layer optical property from a user input list. Example: this surface has total difference between the associated node numbers of 200,000, but the top optical property on this one-sided element is black paint. MLI isn't painted
Notes: Brian

## Slide 46: Overlapping Surfaces Clean-Up Output
This lister prints out all of the overlapping surfaces from TD's output but cleans up obvious duplicates. User then dispositions the list by searching for the surface name (i.e., EF0C5) in the model browser and examining each pair. In this case, we dispositioned anything over 10% overlapping as below:
The tool also lists the temperatures of the respective surfaces and highlights surfaces that have significant T^4 ratios or emissivity values for which an object poking through another, even at a low overlap percentage, could be a problem. In this example, these highlighted overlaps are well below the threshold of 10% that we were individually checking via TD, but could still be a problem.
Notes: Brian

## Slide 47: FilePlottingTools
FilePlottingTools is an Excel-based VBA tool
Allows rapid plotting of registers and temperatures saved to .sav file or .us* files
Use a template excel file to easily compare model output to temperature limits
Available from Langley on request

## Slide 48: Goddard Process for Recent Large Telescope
Additionally, the reviewer keeps a running list of issues as the checklist is worked through. These are given a severity and fix implementation difficulty rating
Reviewer is an outsider to the flight model build
119 individual model checks (with some overlaps)
  Each is individually dispositioned
Notes: Brian

## Slide 49: Goddard Output for Recent Large Telescope
Summary slide shows model version, other documentation reviewed, and a quasi risk square with green being a non-critical and easy to correct issue, and red being a really critical, very hard to fix problem with the model.
The top 5 issues are listed for the modeler to consider.
This, the tools, and the checklist/issue list are given to the modelers for disposition and discussion.
Notes: Brian

## Slide 50: Langley OneNote Model Review Template

## Slide 51: Other Model Checks
TVAC balances provide a check of the model
Even times of powering on the system in air or during TVAC transitions can be useful for the analyst to get a first look at the model behavior
Notes: Brian

## Slide 52: Conclusions
Model checking should be a standard practice for missions at all levels
  Level of rigor might depend on the complexity and scope of the project, from self checks to peer checks to independent checks
This presentation has provided an in-depth set of checks to make
  This full list could take weeks on a complicated model
  However, even casual model checks can be useful, especially if done as the model is being built
We hope that this presentation can help all of us catch modeling errors early and improve the overall accuracy of our predictions
Notes: Brian