## Slide 1: MLI Standards and Best Practices
Presented By Aerothreads
Thermal & Fluids Analysis Workshop TFAWS 2018 August 20-24, 2018
NASA Johnson Space Center
Houston, TX
TFAWS Passive Thermal Paper Session

## Slide 2: About Us
Aerothreads specializes in
Multi Layer Insulation (MLI):
Consultation
Design
Fabrication
Installation
Critical Support Services
Notes: Good Morning
Myself – Lead thermal blankt specialist
Aleks Bogunovic - CEO
Casey Kelby – Thermal Engineer
Aerothreads specializes in multi layer insulation: Consultation, Design, Fabrication, Installation and Critical Support services
We are a Women Owned SB and a SBA Certified HUBZone SB located in College Park MD

## Slide 3: Outline
Section 1 – MLI Overview
  Design, fabrication, installation
Section 2 – Requirements, Design considerations, and Best Practices
  Thermal
  Mechanical
  Contamination
  Electrical
  Material
Section 3 – MLI Trends
  MMOD
  Cryogenic
  Space Station/Beta-cloth
  Exotics

## Slide 4
Section 1 – MLI Overview

## Slide 5: MLI Overview
Design and templating
  Mechanical drawing
  CAD model
  Rapid prototypes
  Flight hardware
Notes: First step: design and templating is the most critical and time consuming step in blanketing.
-MLI design begins from either: mechanical drawing, CAD model, rapid prototypes or flight hardware
-Create the templates by hand using melinex, an anti-static clear poly film
-templates are then fit-checked on hardware and modified for proper fit and to mark any cut-outs, slits, protrusions, harnessing, or anything else that could affect the fit of the blanket
-This process is a lot like draping material for clothing…a lot of design considerations only come up when you are physically working on the hardware and are able to problem-solve on the spot
The further away from flight-like the hardware is in when we template, the greater the impact in later fit, modifications, and function of the MLI. We can start with CAD files to reduce time spent on the hardware or travel if you are located outside of the MD area, but often times there are components that are not represented in CAD models. Final template design should be fit checked on flight hardware in flight configuration before beginning MLI fabrication.

## Slide 6: MLI Overview
Fabrication
  Formed vs. flat
  Sewn overlays
  Built to print
Installation
  Test
  Flight/pre-ship
  Launch support
Notes: -Aerothreads fabricates all of our blankets on a form, unless specifically required to fab. flat
-This ensures that all layers and shift around every corner and shape that the blanket takes, which eliminates any potential compression/shorting of the blanket
-We use various forms and techniques to cut the blanket in shape, as well as edge-tape the MLI in the formed position. This ensures that every layer of the blanket layers perfectly inline with the others, making superior fit and function of the MLI(see pic on left)
-MLI is typically edge-taped with tape that matches the outer-layer of the blanket. Some blankets require a sewn overlay, or stitched Velcro, those blankets are stitched on an industrial machine and finished by hand
-We also support installation of MLI for test, flight, and for final launch-site close-outs
-For test, MLI can be installed so it can be more easily removed and with access requirements specific for GSE
-ideally the majority of blankets are closed-out prior to thermal vacuum testing, only leaving points for shipping access or launch-site testing
-Final installations include: grounding to the hardware, securing mechanical fasteners, seam-taping to control directional venting, and an overall engineering walk-thru to ensure flight readiness
-Final closeouts for launch readiness include: verification of grounding, any final close-outs, and an overall inspection

## Slide 7
Section 2 – Requirements, Design Considerations, and Best Practices

## Slide 8: Thermal Requirements
Areas to be blanket
Radiator surfaces
MLI materials and layup
High-temperature, cryogenic, and other specialty MLI requirements
Notes: Areas to be blanketed: where MLI begins and ends, critical areas, places to avoid overlaps

## Slide 9: Thermal – Design Considerations
  Thickness of layup
    Keep-out zones, tight clearances
  High-temperature
    Adhesive concerns
    Stitched construction
  Cryogenic
    One-time installation, access considerations
    Overlap thickness
  Material fragility
    Sensitive outer layers
    Material thickness
Notes: Thickness of layup: Known ahead of time, can influence how the MLI is designed. If the layup is especially thick, like pictured, being aware of tight clearances is important. Thicker blanket = harder to make complex, form-fitting MLI
Temperatures ranges can affect the type of adhesive that is used. Stitched construction can be used to mitigate tape failing concerns if there are extreme temperature ranges.
Cryogenic requirements call for more critical MLI design. Typically cryo MLI are a one-time installation, once they go on they cannot come off without ruining the blanket. Layer to layer or shell-to-shell closeouts also increase thickness in overlap areas.
Specialized outer layers can require different techniques in order to preserve fragile coatings on the film. Fabricating with a protective cover, fabricating sets of MLI for test and flight spares, can all help minimize damaging the film. Thinner outer layers are more fragile than something heavier, and depending on the use (how many times the blankets are opened, need to come on and off, etc) using a thicker/thinner outer material should be considered.

## Slide 10: Mechanical Requirements
Access
  Harness ports
  Lift points
  Optical cubes
  GSE accommodations
  Integration
  Keep-out zones
Mechanisms
  Gimbals
  Hardware interfaces
Notes: Mechanical requirements affect the design and fabrication of MLI. Once MLI is installed, it can block access to: Harness ports, lift points, optical cubes, GSE accommodations, launch locks. MLI can be designed to accommodate these features, and being aware of them while designing and templating the MLI is critical.
Understanding the integration flow with mechanical hardware as well as keep-out zones also affects the design and planning of MLI.
Mechanisms can create unique considerations when it comes to MLI. Gimbaled hardware, tight clearances, and interfaces require more complex designs, precision fabrication, and skilled integration.

## Slide 11: Mechanical – Design Considerations
MLI attachment/bonded fasteners
  Buttons (G-10)
  Click-bonds
  TC 105s
  Velcro
  Dual Lock
  Custom
  Snake bites
Hardware accommodations
  Where can MLI attach to?
  Flaps, overlaps, design additions for access points
  MLI designed to accommodate integration flow
Notes: There are many ways to attach MLI to the hardware. Fasteners allow the blanket to either be attached directly to the hardware, or fastener to itself so the blankets are relying solely on tape. Depending on hardware, location of MLI, clearances, and blanket material these are the options that should be considered
Hardware accommodations –
Especaially when it comes to complex mechanical designs, determining where MLI can attach to

## Slide 12: Contamination Requirements
Vacuum bake-out
  Pre-fabrication
  Post-fabrication
Venting
  Filtered vents
  Directional venting
  Internal materials
    Perforated layers
Notes: Cleanliness: white light inspection, black light inspection, IPA wipe, nitrogen purge ,bagging requirements..etc etc
-limitations: velcro

## Slide 13: Electrical Requirements
Grounding standards
  J-Standard
  NASA Standard
  Customer specified
Operating environment
  Material considerations
Hardware ground locations
Notes: LEO – more surface charging

## Slide 14: Electrical – Design Considerations
Grounding/bonding:
  Soldered or crimped lugs
  Redundancy
  Ground wire resistance requirement
  # of grounds per MLI
  SLI grounding
Operating Environment
  Outer layer/coatings
  Conductive adhesive
Ground locations
  Hardware accommodations
  Integration sequence
  Pin/socket (for access)

## Slide 15: Material Selection – Common Materials
Specialized Outer Layers
  Metallized Polyimide (Kapton HN)
  Carbon filled Polyimide (Kapton XC & CB)
    Metallized (VDA)
    Stamet
  FEP (Teflon)
    Metallized (VDA)
    Silver / Inconel

## Slide 16: Material Selection – Common Materials
Inner Layer Options
  Polyester or Polyimide
    0.25 mil PET
    0.30 mil Polyimide (Kapton HN)
  Spacer options
    Netting
    Embossed inner films

## Slide 17: Material Selection – Considerations
Storage
  19 deg C +/- 9 deg C (65 deg F +/- 15 deg F)
  50% RH +/- 10%
  Suspended cores for shipping, boxed storage in original packaging materials
Packaging
  Utilize heat sealed bags with desiccant and humidity indicator cards
  Nitrogen purge for sensitive coatings

## Slide 18: Material Selection – Considerations
Shelf life
  12 month shelf life
  Known aging of coatings and adhesives
Coating fragility
  Germanium
  Indium Tin Oxide (ITO)
  Vacuum Deposited Aluminum (VDA), Stamet, Silver/Inconel

## Slide 19
Section 3 – MLI Trends

## Slide 20: MLI Trend - MMOD
Material Considerations
  Material lead time
  Material thickness
  Rigidity
  Mass
  Boxier designs
Micrometeoroid Orbital Debris (MMOD)
  Stand-off from hardware
  Spacing
  Sewn MLI
  Whipple shield

## Slide 21: MLI Trend - Cryogenic
Cryogenic MLI Considerations
  Material lead time
  Layup thickness
  Layer-to-layer closeout vs. shell-to-shell
  Access to hardware
  Installation sequence
  One-time use
  Grounding schematic
  Longer design, fabrication, and installation time

## Slide 22: MLI Trend – Space Station/Beta cloth
Considerations
  Material lead time
  Layup thickness
  Sewn construction
  Reinforced inner layer
  Accessibility
  Modifications (limited ability)
  Grounding requirements
  Complexity of MLI
  Hand-stitch/fastener use instead of tape

## Slide 23: MLI Trend – Exotic Material
Stamet/GBK
  Material lead time
  Handling considerations
  Cost
  Protective layers
  Conductive tape
  Cleaning considerations
New photo

## Slide 24: Questions?