## Slide 1: Thermal Modeling and Test Correlation for SWOT Loop Heat Pipe Evan Shea Orbital ATK
Presented By Evan Shea
Thermal & Fluids Analysis Workshop TFAWS 2016 August 1-5, 2016
NASA Ames Research Center
Mountain View, CA
TFAWS Passive Thermal Paper Session
Orbital ATK IPWG Approval 657, Unlimited Release

## Slide 2: Overview and Objective
Overview
  Characterizing the transient behavior of a loop heat pipe (LHP) is difficult to do accurately. This poses a design challenge when a LHP is required to operate in a situation where transient performance is the limiting design case.
  The Surface Water Ocean Topography (SWOT) mission, managed by JPL, presents a need for a LHP that can maintain a tight payload temperature stability during fast radiator transients (0.05C/min of the payload)
    For SWOT a benchtop LHP was tested by JPL to characterize its ability to maintain the stability requirements, and then a Thermal Desktop model was developed and correlated to this test data.
Objective
  Use SWOT as a working example to discuss a method for creating simple transient LHP models in TD and Sinda/Fluent
  Review the initial results of the SWOT benchtop model
  Discuss advantages of using early benchtop testing/modeling to demonstrate LHP transient performance.

## Slide 3: Loop Heat Pipe Background
Heat is applied to the evaporator which contains the primary wick which is saturated with liquid
Vapor is generated at the evaporator and then travels to the condenser
In the condenser the vapor condenses transferring heat to the radiator surface
Liquid exits the condenser where it returns to the evaporator
Excess liquid is stored in the reservoir which is connected to the evaporator by a secondary wick
Wick
Hot Vapor
Liquid
Heat Rejected Out
Heat In
Compensation Chamber

## Slide 4: SWOT Benchtop LHP System
Condenser
Evaporator
Reservoir
Sink
Test Pallet
Thermal Mass 1
4 Heat Pipes
LHP Evaporator Interface
Benchtop system consists of LHP system, a convective cold sink, and a Test Pallet
Test Pallet consists of 4 heat pipes embedded in an aluminum base with 3 thermal masses simulating instruments. All 3 thermal masses have heaters
Thermal Mass 2
Thermal Mass 3
All images on this slide courtesy of NASA/JPL-Caltech

## Slide 5: Model Geometry
Evaporator
Reservoir
Test Pallet
Radiator
Heat Pipes
Evap/Test Pallet Interface
Transport
Lines
Condenser Lines
Generating model geometry is the first step.
  Majority of the model is simple pipe and surface/solid geometry.
Evaporator and Reservoir
  Evaporator and reservoir were modeled with simplified geometry due to the system level nature of this model
  Evaporator/Reservoir fluid modeling performed with CAPPMP
Heat Pipe
  Heat pipe structure is not modeled, instead their mass is accounted in the Test Pallet base
Working Fluid
  Propylene is the working fluid. C&R tech property files were used on the model

## Slide 6: Thermal Model Schematic
Evaporator is modeled as 4 nodes
  Evaporator nodes are connected to a node representing LHP saturation temperature.
  Evaporator conductance was correlated from test data
Reservoir
  Reservoir fluid is modeled as a single tank lump.
  This lump is also connected to the saturation node by a conductor representing wick back conduction.
  Back conduction was correlated from test data
FLOW.7100
  This lump represents the 100% vapor output from the primary wick.
CAPPMP Junction
  CAPPMP is a built in capillary pump submodel that is used to model the primary wick
  CAPPMP connects the Reservoir node with the vapor outlet
  This subroutine takes heat input (in this case through the saturation node) and creates the appropriate vapor generation from the res.

## Slide 7: CAPPMP Notes
Primary CAPPMP inputs
  Capillary Flow Conductance (CFC)
    This is the permeability of the primary wick. For SWOT wick test data was used
  Capillary Ratio (RC)
    This is the pore size/radius. This was left as zero for this model to improve stability and runtime
CAPPMP can be temperamental to use and is easy to crash or have inefficient runs
  Setting the RC to 0 keeps the CAPPMP from depriming prematurely or in unrealistic situations.
A Wick iface can be used to help the stability of the CAPPMP, but it was not used in this model
CAPPMP is directional so the reservoir and vapor lumps must be placed in the correct order

## Slide 8: Back Conduction
Back conduction is the heat flow rate that occurs between the saturated vapor in the evaporator to the reservoir.
Back conduction has a heavy influence on the amount of subcooling the loop requires to operate
This model uses the classical definition of back conduction
The back conduction conductor must be programmed in Sinda to recalculate at every iteration of the run as it is a function of the pressure drop in the loop and the pressure/temperature saturation curve
Back conduction can be heavily influenced by the design and manufacturing of the evaporator and so must be correlated with test data to insure accuracy. A correction factor is used in the SWOT model for the correlation

## Slide 9: Heat Pipe Model
4 Constant Conductance Heat Pipes were used in the test pallet to act as a thermal spreader
Heat pipes were modeled as conductors attached to an arithmetic node that represents the internal vapor of the heat pipe
  Evaporator and condenser conductance's determined from previous testing done at OA facilities
  This method assumes that the vapor is isothermal and does not experience any heat loss
This modeling method was chosen because the heat pipes simply being used as spreaders, and their exact behavior is not a point of interest

## Slide 10: SWOT Test Overview
Test Performed by JPL
  Start Up
  Long duration steady state with 200W on the test pallet
  Sink transient (8C/min for ~3 minutes)
  Shutdown
Testing was performed at ambient conditions using a convective/radiative sink
Only the steady state and sink transient were used in model correlation
  The model is not designed to demonstrate start up or shut down operations
Sink transient is designed to test the temperature stability of the interface of thermal mass 1 and 2 to the test pallet.
Data presented in this slide references: Somawardhana, Ruwan. “Thermal Stability Testing of Two-Phase Thermal Control Hardware for the Surface Water Ocean Topography Mission”. International Conference on Environmental Systems (ICES). 2016

## Slide 11: Correlation Parameters
Primary Correlated Values
  Evaporator Conductance
  Back Conduction
  Sink to Radiator Conductance
  Interface Conductance
Measured Property Values
  Wick Permeability
  Wick Pore Size (this is used for Sinda calculations that do not directly affect the model)
  Heat Pipe Conductance

## Slide 12: Sink Transient
200W is applied to the test pallet throughout test
Transient is preceded by long steady state at -63C sink
Sink ramp rate is ~8C/min for 3 minutes
Sink temperature is graphed on secondary axis
Primary interest is in the stability of the Instrument Interface temperature
JPL Test Data
Model Data
Data presented in this slide references: Somawardhana, Ruwan. “Thermal Stability Testing of Two-Phase Thermal Control Hardware for the Surface Water Ocean Topography Mission”. International Conference on Environmental Systems (ICES). 2016

## Slide 13: Thermal Pallet Stability
Initial rate of change of the model synchs up well with the test data
  After initial transient response, the test system stabilizes while the model overshoots before beginning to recover
Model prediction still meets required interface stability

## Slide 14: Model Stability Sensitivity
Model shows relatively small effects of ramp rate on stability
  Above 8C/min there seems to be an exponential degradation in interface stability
Requirement = .05C/min

## Slide 15: Model Limitations
Model does not include the secondary wick
  Model does physically model the secondary wick. Sinda code can be added to calculate secondary wick performance needs, but was not needed for this application
CAPPMP implementation is relatively “dumb”
  The CAPPMP model does not determine when dryout occurs. Sinda code is added to track the pressure drop within the loop. Pressure performance must be checked after the run is complete
Not designed to model Start Up and Shut Down transient cases
Correlation is rough
  Testing was not done with model correlation in mind and was limited in scope.
  Testing was done in an ambient environment adding more uncontrolled parasitics
  Conduction between the sink and radiator is done with a linear conductor due to difficulty in obtaining accurate convection correlation
Model is relatively simple
  The model is relatively simple and will not take into account more complicated phenomenon

## Slide 16: Conclusion
Conclusion
  The as correlated model shows good correlation with test data and can provide reasonable transient predictions.
  The correlated evaporator model can be adapted to evaluate new condenser designs and routing
    This will provide more accurate results then an uncorrelated model
  A simple testbed LHP verifies the SWOT program’s transient performance requirements can be met by this LHP design and a thermal model to help finalize designs.
Future Work
  Update the current SWOT model with variations in condenser design
  Model and correlate the final SWOT LHP designs

## Slide 17: Questions
Acknowledgements
Michael Nikitkin (Orbital ATK) for providing technical and moral support
Ruwan Somawardhana, SWOT Payload Thermal Lead, NASA Jet Propulsion Laboratory, California Institute of Technology - Technical Monitor

## Slide 18: References
Khrustalev, D. “Modeling Transient Operation of Loop Heat Pipes using Thermal Desktop”. Thermal & Fluids Analysis Workshop (TFAWS) 2007
Kim Wrenn, Ed Kroliczek, and Dave Wolf. “Secondary Wick Limitations on LHP Operations”. International Two-Phase Thermal Control Technology Workshop 2001
Somawardhana, Ruwan. “Thermal Stability Testing of Two-Phase Thermal Control Hardware for the Surface Water Ocean Topography Mission”. International Conference on Environmental Systems (ICES). 2016
C&R Technologies. User’s Manual Sinda/Fluint Version 5.7. Boulder: CRTECH, 2014
Khrustalev, Dmitry. “Advances in Transient Modeling of Loop Heat Pipe Systems with Multiple Components”, Space, Propulsion & Energy Sciences International Forum (SPESIF) 2010, Laurel, MD, Applied Physics Laboratory, March 18-20, 2010
Cullimore, Brent and Bauman, Jane, Steady State and Transient Loop Heat Pipe Modeling : International Conference on Environmental Systems (ICES), 2000, SAE 2000-01-2316