## Slide 1: Passive Thermal Coating Observatory Operating in Low-Earth Orbit (PATCOOL) Kevin Bauer NASA Launch Services Program
Presented By Kevin Bauer
Thermal & Fluids Analysis Workshop TFAWS 2020 August 18-20, 2020
Virtual Conference
TFAWS Passive Thermal Paper Session

## Slide 2: Agenda
Background
Mission Objectives
Thermal Design
Modeling Approach
Thermal Desktop Model
Temperature Predictions

## Slide 3: Background
Ideal thermal control coating (TCC) designed for 1 astronomical unit (AU) from the sun and far away from any IR sources first suggested in 1961 by Hibbard
State-of-the-art includes white paints and second surface mirrors
Reflecting most of the suns irradiance while permitting far-IR emission
Scattering white pressed powder with a metallic backing developed at Kennedy Space Center (KSC)
Long-term exploration to the moon, mars, and beyond
Enabling technology advancement for cryogenic fluid storage or even superconductors
[1] Hibbard R. R., “Equilibrium Temperatures of Ideal Spectrally Selective Surfaces,” Solar Energy, Vol. 5, No. 4, Oct. 1961, pp. 129–132.
Notes: Hibbard R. R., “Equilibrium Temperatures of Ideal Spectrally Selective Surfaces,” Solar Energy, Vol. 5, No. 4, Oct. 1961, pp. 129–132.
White paints are scattering particles held together by a binder (alpha 9% epsilon 90%) second surface mirrors transparent to the suns radiation but not IR with a metallic reflector (alpha 9% epsilon 91%)
White paint absorbs 15% solar spectrum TCC absorbs .2%
Proposed coating, low absorption high emittance
In accordance with space policy directives

## Slide 4: Mission Objectives
PATCOOL will serve as a performance test for a TCC developed at KSC
  Comparison to current state-of-the-art thermal control coating AZ-93 white paint
  Incorporate redundancies to reduce uncertainty
Ascertain how close to cryogenic temperatures can the samples reach in a low earth orbit
  Minimize environmental sources to solar radiation
  Collect a significant temperature delta between coatings
Thermal Desktop model validation
  Use of empirical data to improve model fidelity
  How accurate are TCC optical properties?
Notes: Model validation with initial temperature decay after 1800sec as well as orbit oscillation effect
TRL (3-4) from lab testing TRL (5-6) with cubesat mission

## Slide 5: Thermal Design
Thermal control coating samples
  Four aluminum 7075 disks
    - Promote uniformity and isolate coating contribution
  Two coated with AZ-93
  Two coated with a thermal control coating developed at KSC
Sample housing
  Shield samples from earth albedo and IR planetshine
    - Housing cover top coated in AZ-93 bottom with reflective coating
  Kevlar strings (diam. = .36mm)
  Reflective surfaces
3U CubeSat
  Zenith pointing towards the sun
  Sample housing adaptor
    - 3D printed Ultem 1000
  Avionics thermal barrier
    - Reflective coating
Notes: Redundancies in temperature measurements and samples
Thermally isolate samples from cubesat

## Slide 6: Thermal Design
Sample and Cover Alignment
Aluminum Samples
Thermal Protection
MLI
Kevlar strings
AZ-93
Ultem Housing adaptor
Thermal barrier (reflective coating)
AZ-93
(reflective coating on all surrounding faces)
(reflective coating on all surrounding faces)
Notes: 20 mm (.7874”) housing cover opening
25.4 mm (1”) sample diameter
3.175 mm (.125”) spacing between sample and housing cover

## Slide 7: Modeling Approach
International Space Station used for low-earth orbit parameters
Environment conditions assumed from [2],[3]
Sample fidelity
[2] Anderson, B. J., C. G. Justus, and G. W. Batts. "Guidelines for the selection of near-earth thermal environment parameters for spacecraft design." (2001).
[3] Gilmore, David G., and Mel Bello. Satellite thermal control handbook. Vol. 1. EI Segundo, CA: Aerospace Corporation Press, 1994.
Case | Solar Constant (W/m2) | Albedo | IR planetshine (W/m2)
Hot | 1414 | 0.36 | 255.522
Nominal | 1367 | 0.28 | 242.903
Cold | 1322 | 0.22 | 230.285
Notes: - ISS orbit period 5560 sec
Samples discretized 9 in angular direction, 5 in radial direction and 3 in height
Kevlar dia. .36mm (.014”)
TC 4 lead wire configuration (dia. = .127mm)(.005”)

## Slide 8: Modeling Approach
Avionics
  ADCS (.825 W)
  Battery (.1 W)
  BeagleBone (1.05 W)
  EPS (.2 W)
  Tranceiver (.175 W)
Notes: Anderson, B. J., C. G. Justus, and G. W. Batts. "Guidelines for the selection of near-earth thermal environment parameters for spacecraft design." (2001).

## Slide 9: Thermal Desktop Model

## Slide 10: Temperature Predictions

## Slide 11: Future Work
Post processing
  Use of subroutines for an overall energy balance on samples
Model Validation through empirical data
  Lab testing only accounts for simulated solar radiation

## Slide 12: Questions?
Thank you for your time and this opportunity!

## Slide 13: Backup Slides