## Slide 1: Tank Sizing Analysis for the Reduced Gravity Cryogenic Transfer Receiver Tank Erin M. Tesny, Daniel M. Hauser, Jason W. Hartwig NASA Glenn Research Center, Cleveland, OH, USA
Presented By Erin Tesny
Thermal & Fluids Analysis Workshop TFAWS 2021 August 24-26, 2021
Virtual Conference
TFAWS Cryothermal Paper Session

## Slide 2: Overview
Tank Chilldown Background
Modeling Overview
  Tank descriptions
  Charge/Hold/Vent procedure
Results
Conclusions
Future Work

## Slide 3: Background
Understanding fluid behavior in microgravity is essential to further development of in-space cryogenic systems
  No current published data on tank chilldown in microgravity
Reduced Gravity Cryogenic Transfer (RGCT) project is designed to investigate tank chilldown in a microgravity environment onboard a parabolic flight
  1 parabolic flight consists of 25 parabolas, 60s each
Current study: what is appropriate tank size to complete chill down during 1 flight given 3 possible different chilldown scenarios?
  Goal is to chill down the tank wall to some target temperature by the end of the flight

## Slide 4: Tank Descriptions
Tank | Description | Dry Mass (kg) | Internal Volume (m3) | MEOP (psia) | Wall Thickness (in)
1A | Lower Limit | 30.2 | 0.225 | 50 | 3/16”
2A | Upper Limit | 79.0 | 0.904 | 64.3 | 3/16”
2B | Upper Limit, Thick-Walled | 158.2 | 0.904 | 330 | 3/8”
Tank Parameters to investigate:
  Small vs. Large Tank Volume
  Thin vs. Thick-walled

## Slide 5: Modeling Approach
Thermal Desktop, multi-node model
Working Fluid: nitrogen
Tank wall material: Aluminum 2219
Fluid in tank is modeled as twin lumps (liquid + vapor)
Bottom fill dip tube injector with top vent
Monitoring liquid temperature, pressure, and average tank wall temperature

## Slide 6: Charge/Hold/Vent Procedure
Charge/Hold/Vent (C/H/V) Chilldown:
  Charge: Supply Valve Open/Vent Valve Closed
  Hold: Supply Valve Closed/Vent Valve Closed
  Vent: Supply Valve Closed/ Vent Valve Open
    Pattern is repeated once every 60s (or once per 1 parabola)

## Slide 7: Different Chilldown Scenarios
Case No. | Parasitic Heat Load? | Flow Rate (gps) | Operation
1 | No | 100 | Charge: 20s/ Hold: 25s / Vent: 20s
2 | Yes | 100 | Charge: 20s/ Hold: 25s / Vent: 20s
3 | Yes | 50 | Charge: 20s/ Hold: 25s / Vent: 20s
4 | Yes | 100 | Charge: 17s/ Hold: 73s / Vent: 30s

## Slide 8: Tank 1A Results
Chart: Tank 1A Liquid Lump Pressure Vs. Time

## Slide 9: Tank 1A Results (Cont’d)
Chart: Tank 1 A Liquid Lump Temperature Vs. Time

## Slide 10: Tank 1A Results (Cont’d)
Chart: Tank 1A Average Tank Wall Temperature Vs. Time

## Slide 11: Tank 1A Results Summary
 | Propellant Used (kg) | Propellant Vented (kg) | Final Average Wall Temp (K) | Time (s)
Case 2 | 36.5 | 27.3 | 99.0 | 1500
Case 3 | 18.5 | 15.5 | 184.0 | 1500
Case 4 | 21.8 | 15.5 | 167.9 | 1500

## Slide 12: Efficiency Parameters
Propellant Efficiency
Thermal Eff.

## Slide 13: Results: Large vs. Small Tank
Tank | Propellant Efficiency |  | 
 |  | Case 3 | Case 4
 | Case 2 |  | 
1A | 41.5% | 20.6% | 42.3%
2A | 25.2% | 16.2% | 28.9%
Case 3 has lowest propellant/thermal efficiency for both tanks
Tank 1A has similar propellant thermal/efficiency whereas Tank 2A has significantly higher thermal efficiency
Delta T factor is most important parameter in determining if tank can be successfully filled after chilldown
  Tank 1A always has lower Delta T Factor than 2A
  Case 2 always has lower Delta T Factor than Case 4
Thermal Efficiency |  | 
 | Case 3 | Case 4
Case 2 |  | 
43.8% | 43.3% | 48.0%
61.0% | 60.6% | 65.7%
Delta T Factor (K) |  | 
 | Case 3 | Case 4
Case 2 |  | 
10 | 23.3 | 38.3
21.8 | 106.8 | 80.7

## Slide 14: Results: Thin vs. Thick-Walled Tank
Case 3 has again lowest propellant/thermal efficiency for both tanks
Both tanks have similar propellant/thermal efficiencies
Delta T factor is most important parameter in determining if tank can be successfully filled after chilldown
  Tank 2A has lower Delta T factor than Tank 2B for all cases
Tank | Propellant Efficiency |  | 
 |  | Case 3 | Case 4
 | Case 2 |  | 
2A | 25.2% | 16.2% | 28.9%
2B | 19.4% | 14.0% | 26.2%
Thermal Efficiency |  | 
 | Case 3 | Case 4
Case 2 |  | 
61.0% | 60.6% | 65.7%
62.3% | 61.7% | 67.0%
Delta T Factor (K) |  | 
 | Case 3 | Case 4
Case 2 |  | 
21.8 | 106.8 | 80.7
107.2 | 157.7 | 148.2

## Slide 15: Conclusions
For parabolic flight pattern, the recommended tank size for an elliptical dome tank is closer to the size of Tank 1A (0.225 m3) rather than Tank 2A (0.904 m3)
Thin-walled tank (3/16”) has higher propellant and thermal efficiency than thick-walled tank (3/8”)
Thin-walled tank similar in size to Tank 1A is recommended for parabolic flight chilldown
  Case 2 chilldown procedure (Charge: 20s/ Hold: 25s / Vent: 20s with a 100gps flow rate) recommended for this tank size

## Slide 16: Future Work
Further narrow down tank size and wall thickness
  Test rig size
  Maximize efficiency parameters
Use of other injectors besides dip tube for chilldown