## Slide 1: Modular Trajectory Analysis Tool for Skip-Out and Aerocapture Maneuvers Bohdan Wesely, NASA ARC, Aerodyne Industries LLC. Periklis Papadopoulos, SJSU Aerospace Engineering Paul Wercinski, NASA ARC

## Slide 2: Project Overview
Project was completed for an M.S. in Aerospace Engineering at SJSU.
A 3DOF trajectory simulation was developed to study multi-pass aerocapture as an orbit insertion technique.
  Initial goal was to compare with traditional, “single-pass” aerocapture.
  Written entirely in MATLAB utilizing modern object-oriented programming techniques.
  While various trajectory software tools already exist, programming a simulation from scratch re-enforces fundamental EDL relevant concepts. The most valuable takeaway from this project has been the learning experience.

## Slide 3: Orbital Mechanics
Cartesian, equatorial reference frame (ECI) was chosen.
2-body, J2 gravity model, no other perturbing body forces on vehicle.
Program utilizes a patched conic method to stitch together trajectory segments and supports three different physics types, coast, atmospheric flight, and propulsive maneuvers.
3DOF, vehicle modeled as a point mass, no rigid body or attitude dynamics.
Solver utilizes a Runge Kutta 4/5th order variable step integrator to solve the equations of motion.
  Widely used technique for trajectory propagation
Position Vector
Gravitational Constant Definition
2-body Equation of Motion
Equation of Motion for Propulsive Maneuvers
Newton’s Universal Law of Gravitation

## Slide 4: Aerodynamics Modeling
The conceptual design nature of this analysis tool necessitated fast, reliable method of estimating vehicle aerodynamics.
Newtonian mechanics are utilized for continuum flow and a Maxwellian particle collision model is used for free molecular flow.
  Newtonian methods have been used since the 1950’s for modeling hypersonic flows over blunt bodies and are utilized by modern tools such as CB-AERO and TRAJ.
Pressure and shear coefficients () depend on local surface inclination angle and various freestream properties.
Analytical expressions can be derived for simple axisymmetric shapes. A sphere-cone consists of concatenated expressions for a sphere and frustrum.
  Expressions are derived by taking the surface integral over the vehicle body.
Moment coefficients can also be computed given a reference length.
Continuum
Free Molecular

## Slide 5: Transitional Aerodynamics
Transitional or rarefied flow has characteristics of both free molecular and continuum flow. A non-dimensional parameter called the Knudsen number is used to define each flow regime.
A general guideline is a defines continuum flow and defines free molecular flow.
  These limits often require case by case refinement and comparison with empirical data.
Transitional flow can be approximated through a bridging function which assumes any local or global aero-coefficient is a weighted average of the free molecular and continuum limits.
  A sine squared bridging function was used for the trajectory sim in this project.
  More advanced bridging functions exist but require a DSMC anchor point at the center of the transitional regime.
Knudsen Number
Mean Free Path
Sine Squared Bridging Function Formulation

## Slide 6: Atmospheric Modeling
The NASA developed Global Atmospheric Reference Model (GRAM) is an engineering design tool that can compute planetary atmospheric conditions utilizing ephemeris calculations and a host of empirical data.
Supported Planets
  Earth, Mars, Venus, Jupiter, Uranus, Neptune, Titan (SaturnGRAM in development)
Key GRAM implementation details
  GRAM model queried at each trajectory time step for maximum accuracy
  Temporal, spatial variations and winds are modeled within GRAM
  Atmospheric uncertainties and perturbations are supported through Monte Carlo runs
  Constant vehicle orientation, 3DOF, no GNC modeling or uncertainties at this point

## Slide 7: Aerothermal Modeling
The Sutton Graves approximation was used as the primary stagnation heating rate metric for this project.
  (convective only)
  Simple, fast, and easy to implement, values for k readily available for various planetary bodies.
Modern Brandis correlations have also been implemented for CO2, N2, and H2/He atmospheres. Often require species mole fractions meaning decreased computational efficiency.
To determine the thermodynamic state at the stagnation point, an iterative process is necessary utilizing the continuity equations.
Shock relations (solved iteratively)
Thermochemical Equilibrium Calculations

## Slide 8: Aerothermal Modeling
The chemical equilibrium calculation is computationally tedious and is employed in the industry standard, NASA developed CEA software.
The trajectory tool as part of this project utilizes symbolic math to reduce the set of non-linear partial pressure equations for fast convergence.
  The NASA ARC TS developed TRAJ code will pre-generate a thermodynamic Mollier diagram for efficiency.
  In many cases, the isentropic pressure ratio (Raleigh-Pitot formula) is a good enough approximation.
The trajectory program supports Monte Carlo runs which can generate a normal distribution of aero heating environments based on trajectory and GRAM atmospheric dispersions.
P1 = 1 Pa
T1 = 216.4 K
0.79 mole N2
0.21 mole O2

## Slide 9: Uncertainty Modeling
A Monte Carlo Analysis was run for a small Venus entry vehicle to test the perturbation capabilities in GRAM.
5000 runs were completed in around 13 mins on a 12-core i9 machine, parallelization possible but not utilized.
Potential use as a margin policy if 3σ edge case aerothermal environments are fed into a material response program.
  Pressure, temperature and species mole fraction dispersions are not yet supported for VenusGRAM.
Monte Carlo Test Case | 
Number of Runs | 5000
Julian Date | 2460809 (14-May-2025)
Mass | 17 kg
Cone Half Angle | 45°
Diameter | 0.43 m
Nose Radius | 0.118 m
Dispersions |  | 
Parameter | Mean | Variance
Velocity | 11 km/s | 1σ=0.05 km/s
EFPA | -10° | 1σ=0.1°
Longitude | 130° | No Dispersion
Latitude | 20° | No Dispersion
Azimuth | 91° | No Dispersion
Winds | GRAM | GRAM 3σ
Density | GRAM | GRAM 3σ
Mean: 1513 W/cm^2
3σ: 208 W/cm^2
Mean: 1.292e5 Pa
3σ: 2.173e4 Pa
Move to Backup

## Slide 10
Trajectory Sample Cases

## Slide 11: Multi-Pass Aerocapture at Venus
A conceptual design space was generated for a low ballistic coefficient multi-pass aerocapture vehicle at Venus.
A “sweet spot” for the initial apoapsis altitude can be found through optimization which for Venus is ~150000-250000 km.
  Low range chosen to allow for deployable TPS options.
Numerous test trajectories were validated against traditional aerocapture studies in literature and with the NASA ARC developed TRAJ program.
Initial orbit apoapsis is 175000 km
Vehicle diameter varied from 2-4 m
Nose radius is ¼ the vehicle diameter
70° Sphere Cone
α=10°/-10°
0°Lat, 170°Long, 150 km
Heating can vary by ~5-7% depending on entry long/lat and JD
Primary Venus Validation Reference:
Lugo, R. A., Dutta, S., Matz, D., Johnson, B. J., Pensado, A. R., Roelke, E., Aguirre, J. T., and Powell, R., “Performance Analysis of SMALLSAT Aerocapture at Venus,” AIAA SCITECH 2023 Forum, Jan. 23–27, 2023, National Harbor, MD. https://doi.org/10.2514/6.2023-0878

## Slide 12: Multi-Pass Aerocapture at Venus
500 km final target science orbit, 4 total atmospheric entries.
A mission planning routine determines the optimal number of atmospheric passes and TCM’s to reach the final target orbit.
The multi-pass offers a narrower range of aerothermal environments that are more benign than the single pass.
A future study might include a Monte Carlo analysis to determine whether a multi-pass approach is less sensitive to atmospheric or trajectory uncertainties.
= 17.55 kg/m^2 at α=0°
Corner radius and backshell geometry not modeled for this run, but are supported by Newtonian panel method
Single Pass, Large Design Range
Multi Pass, Smaller Design Range

## Slide 13: Summary and Next Steps
A Novel EDL mission design tool has been developed that has the capability to study a wide range of entry problems to assess viability.
  The program can optimize and simulate small propulsive maneuvers and con-ops for complex orbital insertion methods such as multi-pass aerocapture.
A stretch goal for this software tool would be to model interplanetary transfers and directly couple aspects like the launch window, launch vehicle, and gravity assists to the aerothermal and entry environment at the destination.
Some technical short-term improvements
  N-body
  SPICE integration
  Translation to Python/C++
  Expanded comparison with TRAJ, additional comparisons with other tools such as POST2, GENESIS,
  6DOF, mass properties, stability
  Expanded radiative heating correlations

## Slide 14: Acknowledgements
Paul Wercinski, NASA mentor, NASA ARC, Entry Vehicles and Systems Branch
  For countless guidance and technical assistance throughout this project.
Periklis Papadopoulos, SJSU Advisor
  For valuable advice and feedback for this project and throughout my M.S. degree.
David Hash, Mairead Stackpoole, Ethiraj Venkatapathy, Todd White, NASA ARC, Entry Systems Division
  For valuable feedback and technical insight during rehearsal presentation.

## Slide 15
Questions?

## Slide 16: Backup
Backup

## Slide 17: Why?
A variety of trajectory simulation software exist such as POST, GENESIS, FAST, etc.
Copernicus and several other tools exist for interplanetary mission design and maneuver optimization.
Most importantly, programming a physics simulation from scratch re-enforces fundamental mathematics knowledge, modeling, and programming techniques that are all relevant to EDL and space systems in general.
  Also, building a completely new codebase/architecture is rare, legacy programs are often used for 20+ years. While they can be continuously updated, there are often fundamental limitations and out of date implementations that remain.
  Bloating out an architecture by adding modules, wrappers, and libraries while leaving original source untouched can lead to lower readability, original authors often retire or move on.
At its core, 2-body gravitational mechanics isn’t that difficult to simulate in a modern development environment like MATLAB or Julia.
Additional fidelity and physics can easily be added without starting over or throwing off the existing models.
While traditional aerocapture has been simulated numerous times in literature, a simulation combining multiple atmospheric entries, propulsive maneuvers, and trajectory optimizations is not as common.

## Slide 18: Multi-Pass Aerocapture at Venus
Several planetary bodies were evaluated for the benefits of a multi-pass approach.
  Uranus and Neptune, while popular for traditional aerocapture, aren’t applicable for a multi-pass apoapsis reduction due to the presence of natural satellites for free down-pumping maneuvers and limited science at ultra low orbits.
  The Uranus moon Titania orbits at ~550,000 km, which is near the ΔV limit of a bonded elliptical orbit.
Venus has no natural satellite and has ample science objectives in low (~500 km) orbits. The trajectory tool was used to explore the feasibility of a small-sat, multi-pass aerocapture mission.
A weighting function was used to evaluate the optimal aerocapture post-exit altitude based on stagnation heating rate and orbital period.

## Slide 19: Multi-Pass Aerocapture at Venus
One of the drawbacks of a multi-pass approach is increased mission duration.
  Orbital period varies non-linearly with apoapsis altitude.
Shaving off less ΔV will produce a milder aerothermal environment but also a higher apoapsis and longer orbital period.
  A “sweet spot” can be found through optimization which for Venus is an apoapsis of ~150000-250000 km.
Using this data, a conceptual design space can be generated for a low ballistic coefficient aerocapture vehicle at Venus targeting a 500 km science orbit.
Initial orbit apoapsis is 175000 km
Vehicle diameter varied from 2-4 m
Nose radius is ¼ the vehicle diameter
70° Sphere Cone
α=10°/-10°
0°Lat, 170°Long, 150 km
Heating can vary by ~5-7% depending on entry long/lat and JD
Low range chosen to allow for deployable TPS options
Primary Venus Validation Reference:
Lugo, R. A., Dutta, S., Matz, D., Johnson, B. J., Pensado, A. R., Roelke, E., Aguirre, J. T., and Powell, R., “Performance Analysis of SMALLSAT Aerocapture at Venus,” AIAA SCITECH 2023 Forum, Jan. 23–27, 2023, National Harbor, MD. https://doi.org/10.2514/6.2023-0878

## Slide 20: Venus Multi-Pass Additional Results
Maneuvers Summary |  | 
Maneuver | Duration (s) | ΔV (m/s)
Lift Up |  | 
Interplanetary TCM | 10.49 | 0.525
1st Periapsis Adjust | 0.128 | 0.006
2nd Periapsis Adjust | 2.000 | 0.100
3rd Periapsis Adjust | 10.15 | 0.507
Final Periapsis Raise | 190.0 | 116.3
Lift Down |  | 
Interplanetary TCM | 12.17 | 0.610
1st Periapsis Adjust | 0.194 | 0.010
2nd Periapsis Adjust | 2.141 | 0.110
3rd Periapsis Adjust | 8.137 | 0.407
Final Periapsis Raise | 177.1 | 108.2
Totals | Lift Up | Lift Down
Mission Duration (days) | 5.461 | 5.468
Maneuvers ΔV (m/s) | 117.4 | 109.4
Propellant Usage (kg) | 7.832 | 7.304
Interplanetary Orbital Elements | 
Parameter | Value
Eccentricity () | 1.3074
Semi Major Axis () | -2.0005e4 km
Inclination () | 0°
Argument of Periapsis () | 0°
Long. of Ascending Node () | 0°
True Anomaly () | 137°
Hyperbolic Excess Velocity | 4.0298 km/s
Julian Date | 2455504
Initial Target Apoapsis (km) | 200000
Interplanetary Orbital Elements | 
Parameter | Value
 | 1.3074
 | -2.0005e4 km
 | 0°
 | 0°
 | 0°
 | 137°
Hyperbolic Excess Velocity | 4.0298 km/s
Julian Date | 2455504
Initial Target Apoapsis (km) | 200000
Aero-Pass Summary |  |  | 
Pass | (W/cm^2) | (J/cm^2) | ΔV (km/s)
Lift Up |  |  | 
Insertion | 70.05 | 4022 | 0.916
1st Pass | 53.74 | 3645 | 0.914
2nd Pass | 39.55 | 3350 | 0.912
3rd Pass | 26.58 | 3340 | 0.892
Lift Down |  |  | 
Insertion | 61.66 | 4416 | 0.916
1st Pass | 46.05 | 4085 | 0.915
2nd Pass | 32.30 | 3903 | 0.914
3rd Pass | 19.22 | 4445 | 0.912
Aero-Pass Summary |  |  | 
Pass |  |  | ΔV (km/s)
Lift Up |  |  | 
Insertion | 70.05 | 4022 | 0.916
1st Pass | 53.74 | 3645 | 0.914
2nd Pass | 39.55 | 3350 | 0.912
3rd Pass | 26.58 | 3340 | 0.892
Lift Down |  |  | 
Insertion | 61.66 | 4416 | 0.916
1st Pass | 46.05 | 4085 | 0.915
2nd Pass | 32.30 | 3903 | 0.914
3rd Pass | 19.22 | 4445 | 0.912
Figure 6.15 Venus Deployable TPS Additional Trajectory Views
Spacecraft Input Parameters | 
Parameter | Value
Initial Mass | 200 kg
High Thrust System | 120 N
Low Thrust System | 10 N
ISP (both systems) | 300 s
Trim Angle of Attack (α) | 10°/-10°
at α=10°/-10° | 1.550
at α=10°/-10° | 0.237
Diameter | 3 m
Nose Radius | 0.75 m
Sphere Cone Angle | 70°
at α=0° | 17.55 kg/m^2
at α=10°/-10° | 18.26 kg/m^2
Final Target Altitude | 500 km
Spacecraft Input Parameters | 
Parameter | Value
Initial Mass | 200 kg
High Thrust System | 120 N
Low Thrust System | 10 N
ISP (both systems) | 300 s
Trim Angle of Attack (α) | 10°/-10°
 | 1.550
Diameter | 3 m
Nose Radius | 0.75 m
Sphere Cone Angle | 70°
 | 17.55 kg/m^2
 | 18.26 kg/m^2
Final Target Altitude | 500 km

## Slide 21: Multi-Pass Aerocapture at Venus
Single Pass, Large Design Range
Multi Pass, Smaller Design Range
An adaptive mission planning module was developed for the trajectory program that determines the optimal number of atmospheric passes to reach the final target orbit.
  The program balances the ΔV of each pass with the bounding initial orbital insertion
  Periapsis correction maneuvers are optimized and executed after each pass
  A final periapsis raise maneuver is executed after the final target apoapsis is achieved.

## Slide 22: Peak Heating and Orbital Period Tradeoff
Figure 6.5 Peak Stag. Heat Flux to Orbital Period Tradeoff
1 m diameter, 0.25 m nose radius
BC = 138 kg/m^2
60° Sphere Cone
11 km/s Venus entry

## Slide 23: Monte Carlo Test Case Additional Details
Mean: 2.4325e+04 J/cm^2
3σ: 2.8471e+03 J/cm^2

## Slide 24: Atmospheric Modeling
Venusian winds modeled within GRAM were studied in detail.
  The winds on Venus are significant at higher altitudes (<200 m/s) and are faster than the planet’s rotation.
GRAM outputs winds in three components, north to south (nsw), east to west (eww), and vertical (vw) in the east, north, zenith (ENZ) frame.
  A great deal of time was spent in reference frame conversion handing and efficiency for this project (QXx is the ENZ to ECI conv. Matrix).
Venusian Wind Magnitude and Direction (JD 2459138)
Coriolis Effect
Winds

## Slide 25: Atmospheric Modeling
With a sufficiently blunt body (~60° half angle) the vs. lift slope is reversed compared to a slender body or traditional airfoil. The same analogy applies for sideslip .
This effect results in the entry vehicle being pulled in the direction of the wind, almost like a sailboat sailing upwind.
  Crosswind and tailwind trajectory dispersions were tested for a small 60° sphere cone entry vehicle at Venus.
  Effect is significant for Aerocapture post-exit altitudes.
Polar Orbit
V = 11/km/s, Alt = 150 km, Fpa = -5.61°
Final Azimuth (Winds): 173.257°
Final Azimuth (No Winds): 174.242°
Equatorial Orbit
V = 11/km/s, Alt = 150 km, Fpa = -5.61°
Final Altitude (Winds): 828.1516 km
Final Altitude (No Winds): 375.0636 km

## Slide 26: Atmospheric Modeling
Long: 225, lat: 60, Date: 2020, 5, 12, 16, 0, 0.0

## Slide 27: Gridding Methods
Both the free molecular and continuum aerodynamics depend on the local inclination angle of the vehicle surface.
Analytical expressions exist for simple shapes, however for this project a CB-AERO style grid generator was developed to allow for more complex geometries in the future.
The coefficients form an expression for the perturbing acceleration vector due to aero forces. This is a simple addition to the equations of motion, additional perturbations due to spherical harmonics or solar radiation pressure can also be added.
Blunt Body Side View Discretization
Nose View Discretization
Perturbing acceleration vector, coordinate transformation from relative velocity frame (VFR) to ECI frame not shown here for simplicity

## Slide 28: Panel/Grid Method Expanded Relations
Radial Segment Expressions
Circumferential Segment Expressions

## Slide 29: Free Molecular Flow Expressions

## Slide 30: Panel/Gridding Method Convergence
Figure 9.5 Normal Force vs. Number of Divisions (60° sphere cone)
Figure 9.6 Axial Force vs. Number of Divisions (60° sphere cone)

## Slide 31: Panel/Gridding Method Convergence
Figure 9.7 Side Force Convergence (60° sphere cone)
Figure 9.8 Axial Force vs. Number of Divisions (25° sphere cone)

## Slide 32: Reference Frames Overview
Planetocentric vs. Planetodetic is important and must be considered in modeling!
Geocentric is planetocentric referring to “Earth”, often used incorrectly.
Figure 4.16 ENZ and ECI Reference Frames [22]

## Slide 33: Reference Frames Overview
Figure 4.18 Inertial Velocity Frame and Forces on Entry Vehicle
Coriolis Effect
Winds

## Slide 34: Validations of Newtonian Panel Method
Grant, M., and Braun, R., “Analytic hypersonic aerodynamics for conceptual design of entry vehicles,” 48th AIAA Aerospace Sciences Meeting Including the New Horizons Forum and Aerospace Exposition, Jan. 4-7, 2010, Orlando, FL. https://doi.org/10.2514/6.2010-1212

## Slide 35: Validations of Free Molecular Panel Method
Figure 9.11 Sphere Drag Coefficient Validation Results
Figure 9.10 Sphere Drag Coefficient Results from [32]
Figure 9.14 Increasing Bi-conic Results from [33]
Kenneth A. Hart, Kyle R. Simonis, Bradley A. Steinfeldt, and Robert D. Braun. “Analytic Free-Molecular Aerodynamics for Rapid Propagation of Resident Space Objects,” Journal of Spacecraft and Rockets 2018 55:1, 27-36 https://doi.org/10.2514/1.A33606
Kenneth A. Hart, Soumyo Dutta, Kyle Simonis, Bradley A. Steinfeldt and Robert D. Braun. "Analytically-derived Aerodynamic Force and Moment Coefficients of Resident Space Objects in Free-Molecular Flow," AIAA 2014-0728. AIAA Atmospheric Flight Mechanics Conference, January 13-17, National Harbor, Maryland, USA 2014. https://doi.org/10.2514/6.2014-0728

## Slide 36: Validations of Free Molecular Panel Method
Figure 9.20 Validation with [36] at α=0°
Figure 9.19 Validation with [36] at α=10°
Richard G. Wilmoth, Robert A. Mitcheltree, and James N. Moss, “Low-Density Aerodynamics of the Stardust Sample Return Capsule, ” Journal of Spacecraft and Rockets 1999 36:3, 436-44. https://doi.org/10.2514/2.3464

## Slide 37: Validations of Free Molecular Panel Method
Shellabarger, E., Scoggins, J. B., Hinkle, A. D., Dutta, S., Deshmukh, R., Patel, M., and Agam, S., “Aerodynamic Implications of Aerocapture Systems for Uranus Orbiters,” AIAA SCITECH 2024 Forum, Jan. 8-12, 2024, Orlando, FL. https://doi.org/10.2514/6.2024-0950

## Slide 38: Trajectory Validations with TRAJ
°
°
°
°
°
°

## Slide 39: Trajectory Validations with TRAJ
Aerocapture Trajectory at Venus | 
Velocity | 11 km/s
Azimuth/Heading | -90°
Longitude | 305.61606°
Latitude | 5.170641°
Julian Date | 2456755
Mass | 150 kg
Cone Half Angle | 60°
Diameter | 1 m
Nose Radius | 0.25 m
Target Apoapsis | 500 km
Results |  |  |  | 
Lift Down | Resulting EFPA (deg) | Peak Convective Heat Flux (W/cm^2) | Peak Radiative Heat Flux (W/cm^2) | Total Heat Load (Conv. J/cm^2)
Lift Up |  |  |  | 
MATLAB (-10) | -5.424 | 382.25 | - | 48521.66
TRAJ (-10) | -5.410 | 326.70 | 11.16 | 43108.42
MATLAB (-15) | -5.368 | 361.27 | - | 54560.16
TRAJ (-15) | -5.354 | 302.84 | 9.320 | 48836.38
MATLAB (-20) | -5.329 | 347.80 | - | 61161.99
TRAJ (-20) | -5.315 | 301.17 | 9.590 | 55053.46
MATLAB (10) | -5.976 | 572.89 | - | 31264.45
TRAJ (10) | -5.962 | 464.67 | 24.49 | 26578.55
MATLAB (15) | -6.248 | 648.38 | - | 28883.92
TRAJ (15) | -6.234 | 518.04 | 32.14 | 24242.16
MATLAB (20) | -6.592 | 735.47 | - | 27123.57
TRAJ (20) | -6.576 | 578.46 | 66.14 | 22462.20
Results |  |  |  | 
Lift Down | Resulting EFPA (deg) | Peak Convective Heat Flux (W/cm^2) | Peak Radiative Heat Flux (W/cm^2) | Total Heat Load (Conv. J/cm^2)
Lift Up |  |  |  | 
 | -5.424 | 382.25 | - | 48521.66
 | -5.410 | 326.70 | 11.16 | 43108.42
 | -5.368 | 361.27 | - | 54560.16
 | -5.354 | 302.84 | 9.320 | 48836.38
 | -5.329 | 347.80 | - | 61161.99
 | -5.315 | 301.17 | 9.590 | 55053.46
 | -5.976 | 572.89 | - | 31264.45
 | -5.962 | 464.67 | 24.49 | 26578.55
 | -6.248 | 648.38 | - | 28883.92
 | -6.234 | 518.04 | 32.14 | 24242.16
 | -6.592 | 735.47 | - | 27123.57
 | -6.576 | 578.46 | 66.14 | 22462.20
Shellabarger, E., Scoggins, J. B., Hinkle, A. D., Dutta, S., Deshmukh, R., Patel, M., and Agam, S., “Aerodynamic Implications of Aerocapture Systems for Uranus Orbiters,” AIAA SCITECH 2024 Forum, Jan. 8-12, 2024, Orlando, FL. https://doi.org/10.2514/6.2024-0950

## Slide 40: Uranus Aerocapture Analysis
Spacecraft Input Parameters |  | Entry State | 
Initial Mass | 4064 kg | Inertial Velocity | 24.5 km/s
Trim Angle of Attack (α) | 17°/-17° | Lift up EFPA | -23.806°
at α=17°/-17° | 1.436 | Lift down EFPA | -23.509°
at α=17°/-17° | 0.378 | Planetocentric Altitude | 4000 km
Diameter | 5 m | Longitude (deg) | 47.5°
Nose Radius | 1.25 m | Azimuth (deg) | -90°
Sphere Cone Angle | 70° | Geocentric Latitude | 37°
at α=0° | 128.4 kg/m^2 | Target Apoapsis Altitude | 500000 km
at α=17°/-17° | 144.1 kg/m^2 | Atmosphere Cutoff | 4000 km
Spacecraft Input Parameters |  | Entry State | 
Initial Mass | 4064 kg | Inertial Velocity | 24.5 km/s
Trim Angle of Attack (α) | 17°/-17° | Lift up EFPA | -23.806°
 | 1.436 | Lift down EFPA | -23.509°
 |  | Planetocentric Altitude | 4000 km
Diameter | 5 m | Longitude (deg) | 47.5°
Nose Radius | 1.25 m | Azimuth (deg) | -90°
Sphere Cone Angle | 70° | Geocentric Latitude | 37°
 | 128.4 kg/m^2 | Target Apoapsis Altitude | 500000 km
 | 144.1 kg/m^2 | Atmosphere Cutoff | 4000 km
α=17°, alt = 310 km, Mach=26.93 | Calorically Perfect (γ=1.45) | Chemical Equilibrium ()
 | 1.4836 | 1.5840
 | 0.0587 | 0.0627
 | 1.4360 | 1.5331
 | 0.3776 | 0.4032
α=17°, alt = 310 km, Mach=26.93 | Calorically Perfect (γ=1.45) | 
 | 1.4836 | 1.5840
 | 0.0587 | 0.0627
 | 1.4360 | 1.5331
 | 0.3776 | 0.4032
Vehicle diameter varied from 4-6 m
Nose radius is ¼ the vehicle diameter
70° Sphere Cone
α=0°
37° Lat, 47.5° Long
JD = 2466659

## Slide 41: Uranus Aerocapture Analysis

## Slide 42: Uranus Aerocapture Analysis

## Slide 43: Uranus Aerocapture Analysis
Lift Down
Lift Up

## Slide 44: CEA Thermodynamic Lookups
McBride, B. J., Zehe, M. J., and Gordon, S., “NASA Glenn coefficients for calculating thermodynamic properties of individual species,” NASA/TP—2002-211556, John H. Glenn Research Center at Lewis Field, 2002.

## Slide 45: Chemistry Symbolic Math Overview (N2/O2)

## Slide 46: Chemistry Symbolic Math Overview (N2/O2)
(solve iteratively for P_N)
(additional constraint for ionization)

## Slide 47: Chemistry Model Validation (N2/O2)
Anderson, John D. Hypersonic and High Temperature Gas Dynamics. 2nd ed., American Institute of Aeronautics and Astronautics, 1801 Alexander Bell Drive, Reston, VA. 2006.
Conditions at 1 atm, Textbook: Fig 11.12, P.541)

## Slide 48: Chemistry Model Validation with CEA
Conditions at 1 atm, Textbook: Fig 11.12, P.541)
P1 = 1 Pa
T1 = 216.4 K
0.79 mole N2
0.21 mole O2