## Slide 1: A Reimagining of the DPLR Code
Dr. Joshua R. Finkbeiner
NASA Glenn Research Center
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Aerosciences Technical Session
Presented by: Josh Finkbeiner

## Slide 2: Motivation
Model laminar-to-turbulent transition in the NASA Ames Panel Test Facility
Develop/validate heat transfer models for high-temperature seals
  Thermal boundary conditions for seal ingestion
  Enthalpy profiles
Gokcen and Alluni (2013) determined that transition occurs within PTF nozzle
Finkbeiner (2021) identified likely location of transition in PTF nozzle
  Transition occurs in vicinity of upstream edge of the boundary conditioning plate
  Became basis for Ph.D. dissertation
Flow
Semi-elliptical PTF nozzle exit
High-temperature seal test article
Refractory frame
High-temperature seal test article installed in PTF

## Slide 3: Description of the DPLR CFD Code
What is DPLR? See Tang (2016)
  Ames-developed hypersonic continuum structured CFD code
  Massively parallel Data Parallel Line Relaxation (DPLR) solver
  Nonequilibrium gas dynamics models
    High-speed Earth and planetary entry
    Hypersonic heating
  Laminar or RANS turbulence models
  NASA Software of the Year (2007)
Supported numerous flight projects (Orbiter, Orion, Mars rovers, etc.)
Significant heritage in modeling arc jet flows

## Slide 4: Panel Test Facility CFD Domain
Note: Slide is animated
Water-cooled wall / radiative equilibrium insulator
Water-cooled edge
Flow
Flow

## Slide 5: Instabilities Developed During Mesh Refinement
Wall spacing iteratively refined to
Mesh design and refinement performed by automated scripting
  Wall spacing
  Mesh stretch ratios
  Number of points in each block dimension
  Elliptic smoothing
Mesh refinement moved OH block corner toward nozzle walls
  High viscous gradients developed along block edges
  Undefined values developed in tangent viscous flux computations
  Crash!

## Slide 6: DPLR Reimplementation History
Started modifying the DPLR code in 2014
  Identified and corrected numerical instabilities
  Added transition modeling capability (e.g., SST-g-Re)
  Improved robustness of build system
DPLR can be difficult to read
  Officially Fortran 90 but more closely aligned with Fortran 77
  Data dependencies are difficult to trace
    Fortran 90 modules used for global variables but not code
    No intent statements
2014 federal furlough required DPLR work stoppage…
…but, an enrolled Ph.D. student could reorganize the code without violating the Federal Anti-Deficiency Act…

## Slide 7: Summary of DPLR Code Reimplementation
Utilized Fortran 2008 conventions (modules, derived types, etc.)
Removed duplicate code – “Don’t Repeat Yourself” [Hunt (2000)]
  2D and 3D solvers combined into a single universal solver
  Code organized into modules, Modules organized into libraries, etc.
Incorporated standard numerical libraries (e.g., LAPACK)
Corrected tangential viscous gradients at edge/corner ghost cells
Implemented kd-tree to accelerate:
  Computation of distance to nearest wall
  Preprocessor interface detection
Implemented lagged communications across DPLR line boundaries
Reorganized turbulence model subsystem into modular library
Accelerated Jacobian computations by storing modal internal energies
Corrected MUSCL stencil implementation near viscous walls
Added mass flux-based subsonic nozzle inlet boundary condition
Added subsonic nozzle initial condition to accelerate solutions

## Slide 8: Finite Volume Method
Solution assumed piecewise constant
  Flow properties stored at cell centers
  Solution updates derived from interpolated values at face centers
Coupled system of algebraic equations
  Inviscid fluxes computed from left and right face-centered properties (vector)
  Viscous fluxes computed from face-centered property gradients (tensor)
Time integration scheme
  Explicit: face-centered interpolations derived from current values
  Implicit: face-centered interpolations derived from future values

## Slide 9: Multiblock Domain Decomposition
CPU 1
CPU 2
CPU 3
CPU 4
CPU 5
Block 1
Block 2
Viscous corner

## Slide 10: Ghost Cells and Boundary Conditions
CPU 2
Farfield
boundary condition
Corner ghost cell
from CPU 1
Ghost cells
from CPU 1
CPU 1
Ghost cells
from CPU 3
CPU 3
Ghost cells
from CPU 4
CPU 4
CPU 5
Corner ghost cell
from CPU 5
(not implemented)
Viscous wall
implicit boundary condition

## Slide 11: O-H Mesh MPI Communication
Decompose
H-grid (corner)
O-grid
H-grid (corner)
O-grid

## Slide 12: Viscous Flux Computation in Domain Corners
Cells (0,2) and (1,0) specified by boundary conditions
Cell (0,0) is undefined
Caused instability as wall spacing was reduced
Edge tangent gradients
Normal gradients
Well-posed throughout domain interior
Well-posed along all boundaries
Straightforward extension of domain stencil
Boundary normal gradients
Tangent gradients
Well-posed throughout domain interior

## Slide 13: One-Sided Viscous Flux Stencils
Applied one-sided finite differences
Benefits
  Avoids referencing edge ghost cells and maintains numerical stability
  Retains second-order accuracy
  Halves number of MPI communications
  Removes hierarchical corner boundary condition logic

## Slide 14: Comparisons
DPLR 3.05 included example configuration cases
  Desktop-scale
  Mixture of dimensionalities, model specifications, etc.
2D 2mm-diameter hemisphere in Mach 11 air
  6-species air
  2-temperature model (stat. mech)

## Slide 15: 2D Cylinder Comparison (DPLR 3.05 example)
DPLR 4.03.1
GRC DPLR
Mach number distributions along

## Slide 16: 2D Cylinder Comparison (DPLR 3.05 example)
DPLR 4.03.1
GRC DPLR
Static pressure distributions along

## Slide 17: Success
Example laminar-to-turbulent DPLR solution of the NASA Ames Panel Test Facility Nozzle

## Slide 18: Reimplementation of DPLR Not Intended as Criticism
“It should be emphasized that the original DPLR software is an excellent analysis tool that has been a cornerstone of modern aerothermal analysis at NASA. The rewrite of this software should not be viewed as a criticism of the original authors of DPLR; rather, it should be seen as a distillation of their original ideas into a more approachable and understandable form. The improved readability and organization of the rewritten code potentially allows the concepts included in the original DPLR code to become even more influential in the CFD community.” [Finkbeiner (2025)]

## Slide 19: Summary
Reimplemented the DPLR code
Utilized modern software conventions
Enabled laminar-to-turbulent transition modeling in wall-bounded arc jets with
Corrected viscous fluxes along domain edges/corners
Implemented numerous corrections and improvements
Demonstrated good agreement in sample case results with original Ames DPLR

## Slide 20: References
Gökçen, Tahir, and Antonella I. Alunni. “On Laminar-to-Turbulent Transition of Arc-Jet Flow in the NASA Panel Test Facility.” Journal of Thermophysics and Heat Transfer 27, no. 3 (July 2013): 549–62. https://doi.org/10.2514/1.T3984.
Finkbeiner, Joshua R. “Modeling Laminar-to-Turbulent Transition in the Panel Test Facility Arcjet.” Journal of Thermophysics and Heat Transfer 35, no. 2 (April 2021): 386–401. https://doi.org/10.2514/1.T6098.
Tang, Chun Y. “Introduction to DPLR.” Thermal & Fluids Analysis Workshop. NASA Ames Research Center, 2016. https://ntrs.nasa.gov/citations/20160010056.
McBride, Bonnie J., Michael J. Zehe, and Sanford Gordon. “NASA Glenn Coefficients for Calculating Thermodynamic Properties of Individual Species.” NASA Technical Paper. Cleveland, OH: NASA Glenn Research Center, September 1, 2002. https://ntrs.nasa.gov/citations/20020085330.
Langtry, Robin B., and Florian R. Menter. “Correlation-Based Transition Modeling for Unstructured Parallelized Computational Fluid Dynamics Codes.” AIAA Journal 47, no. 12 (December 2009): 2894–2906. https://doi.org/10.2514/1.42362.
Finkbeiner, Joshua R. “Modeling Laminar-to-Turbulent Transition in the Panel Test Facility Arcjet.” Ph.D. Dissertation, Purdue University, 2025.
Hunt, Andrew, and David Thomas. The Pragmatic Programmer: From Journeyman to Master. USA: Addison-Wesley Longman Publishing Co., Inc., 2000.

## Slide 21: Introduction
New implementation of the DPLR code
Motivation: Laminar-to-turbulent transition modeling in wall-bounded arc jets
Description of DPLR code
Challenges encountered while modeling arc jet flows
Reimplementation of the code
Case study: Corrections to viscous fluxes along domain edges/corners
Comparisons of sample case results

## Slide 22: Panel Test Facility DPLR Model
6-species air chemistry model (N2, O2, NO, N, O, Ar)
2-temperature nonequilibrium thermodynamics model
  Translational/rotational temperature from statistical mechanics
  Vibrational/electronic temperature from NASA GRC Gordon/McBride tables [McBride 2002]
Turbulence
  Laminar
  Reynolds-Averaged Navier-Stokes (RANS) transition models
    SST-g-Re (Menter SST) [Langtry 2009]
    Imposed location (Menter SST, Baldwin-Lomax)
  required throughout the nozzle
Notes: Mention that this was a heavily-modified version of the DPLR code – more details in the writeup (or ask questions)
The Gordon/McBride tables were easier to implement in the inlet boundary condition

## Slide 23: DPLR CFD Workflow
23
Mesh Generation
Model geometry (CAD)
Check mesh quality
CFD Preprocessing
Discretize domain volume into a mesh
Populate initial guess
Decompose mesh for parallel processing
CFD Solution
Upload, queue, wait for resources
Download results and check for completion
CFD Postprocessing
Compute primitive variables
Generate plots
Check solution “sanity”
Iterate the solution until steady-state
Detect multi-block interfaces

## Slide 24: IHF Nozzle Comparison (DPLR 3.05 example)
DPLR 4.03.1
GRC DPLR

## Slide 25: IHF Nozzle Comparison (DPLR 3.05 example)
DPLR 4.03.1
GRC DPLR