## Slide 1: Formulation of an Uncertainty Analysis Methodology for Computational Fluid Dynamics of External Flows over Launch Vehicles
Avery White and Kyle Hanquist: The University of Arizona
Paul Schallhorn and Michael Harris: NASA Kennedy Space Center
Michael Elmore: a.i. solutions, Inc.
TFAWS 2025
6 August 2025

## Slide 2: Overview
Motivation and Background
Uncertainty Quantification Methods
Uncertainty Analysis
Test Case Description
Results
Future Work

## Slide 3: Motivation and Background

## Slide 4: Motivation
Launch vehicles face various harsh conditions throughout the takeoff sequence and often carry delicate and costly payloads
Ground tests provide valuable information but are often expensive
  Difficult to test the entire launch sequence – data points must be carefully chosen
Computational fluid dynamics (CFD) is used to supplement these ground tests and provide preliminary information
As with any measurement, CFD comes with inherent uncertainty
This work introduces a methodology for quantifying the uncertainty in CFD of launch vehicles without the existence of experimental data
Image from NASA

## Slide 5: Uncertainty Quantification

## Slide 6: Uncertainty Quantification Methods
Methods for calculating uncertainty can be broken down into a few categories:
  Non-probabilistic methods – interval analysis, sensitivity derivatives, fuzzy logic
    Great for small problems, easily implemented
    Not good for large problems, do not provide enough accuracy for aerospace applications
  Probabilistic methods – statistical or non-statistical methods
    Monte Carlo methods – any method that utilizes sequences of random numbers to perform the simulation
      Converges to the exact solution as the number of samples goes to infinity
      Computationally expensive, slow convergence
    Moment methods – Taylor series expansion
      Easily expanded to multiple input parameters, not computationally expensive
      Assumes the mean takes the form of a normal distribution
    Stochastic differential equation methods – add stochastic variables to the deterministic equations
      Can provide more information about higher moments, less computationally expensive than Monte Carlo methods
      Mainly used for structural mechanics problems
For this work, we are using moment methods
  First moment is the mean
  Second moment is the variance

## Slide 7: Uncertainty Quantification Methods

## Slide 8: Adapting the Method of Moments
First order first moment and second order first moment methods involve using a Taylor series expansion about the mean value of a dataset
In order to avoid the assumption that the probability distribution is a normal distribution, a coverage factor is introduced which comes from Student's t-distribution
  This is often used in experimental uncertainty calculations in which limited data is present
  The coverage factor is based on the number of simulations completed for each configuration

## Slide 9: Adapting Other Methodologies
Using methodology developed by Coleman and Steele for experimental approaches on uncertainty quantification
Using methodology developed by Groves for computational fluid dynamics on internal flows
  Payload fairing spacecraft environmental control systems
  Low speed, incompressible flows
Image from Groves et. Al. [1]
[1] Groves, C. E., Ilie, M., and Schallhorn, P., “Computational Fluid Dynamics Uncertainty Analysis for Payload Fairing Spacecraft
Environmental Control Systems,” 52nd Aerospace Sciences Meeting, AIAA Paper 2014-0440, National Harbor, Maryland,
2014. https://doi.org/10.2514/6.2014-0440.

## Slide 10: Uncertainty Analysis - First Order First Moment
The total uncertainty can be found from the numerical (aleatory) uncertainty and the input (epistemic) uncertainty:
For this preliminary work, we will ignore the numerical uncertainty and focus on expanding the uncertainty from the input parameters
For some CFD output, r, being a function of J inputs:
The combined standard uncertainty is given by:
With the uncertainty from the input parameter being the average value of the result
What happens if the input parameter is also based on a set of parameters?

## Slide 11: Uncertainty Analysis - Second Order First Moment
If the input parameters are also based on their own variable parameters, use second order method
If the input parameter, X, is a function of Y additional parameters,
The uncertainty contribution from that input parameter can be written as:
With partial derivatives calculated as follows:

## Slide 12: Test Case Description

## Slide 13: Test Case Description
A simple test case was constructed using a generic launch vehicle with a spherically blunted tangent ogive nose cone

## Slide 14: Mesh Description
Five meshes were constructed using Pointwise's T-Rex technique
  Source with constant cell spacing was used to control coarseness
  Boundary layer was captured using a first cell spacing of 1E-4 and a growth rate of 1.1
  Ten vehicle lengths were included behind the vehicle to capture wake effects
Mesh Number | Source Radius | Source Length | Source Cell Size | Number of Cells
1 | 5 | 75 | 0.5 | 5,006,420
2 | 5 | 75 | 0.1 | 30,177,456
3 | 10 | 75 | 0.5 | 5,663,259
4 | 5 | 100 | 0.5 | 5,076,091
5 | 5 | 100 | 0.1 | 41,972,093

## Slide 15: Mesh Description
Mesh 1 Full
Mesh 1
Mesh 2
Mesh 3
Mesh 4
Mesh 5

## Slide 16: Input Parameters
Mach 2.0 was chosen as an initial starting point
Corresponding altitude of ~30,000 ft
1976 Standard Atmosphere was used to calculate freestream pressure and temperature
[2] Dufrene, A., MacLean, M., Holden, M., Mehta, M., and Seaford, M., “Space Launch System Base Heating Test: Experimental
Operations and Results,” , Jan. 2016. URL https://web.archive.org/web/20190429090136id_/https://ntrs.nasa.gov/archive/nasa/casi.ntrs.nasa.gov/20160001817.pdf.
Image from Defrene et. Al. [2]

## Slide 17: Input Parameters
A total of 10 cases were run for each configuration, this gives us a coverage factor of 1.833
Mesh 1, Mach 2.0, with the Shear Stress Transport turbulence model was used as the baseline case for the analysis
The same mesh was used for both turbulence models – possibly introducing more error
  This is common practice for many CFD users
 |  |  | Configuration | 
Case Number | Parameter |  | 0 Degrees AoA | 6 Degrees AoA
1 | Mesh | Mesh 1 | 1 | 1
2 |  | Mesh 2 | 2 | 2
3 |  | Mesh 3 | 3 | 3
4 |  | Mesh 4 | 4 | 4
5 |  | Mesh 5 | 5 | 5
6 | Boundary Condition | Mach - 5% | 6 | 6
7 |  | Mach +/- 0% | 7 | 7
8 |  | Mach + 5% | 8 | 8
9 | Turbulence Model | Spalart-Allmaras | 9 | 9
10 |  | Shear Stress Transport | 10 | 10

## Slide 18: Results

## Slide 19: Results
The aerodynamic coefficients are output by the CFD solver upon completion
  CL is the lift coefficient
  CD is the drag coefficient
  CMX is the rolling moment coefficient
  CMY is the pitching moment coefficient
  CMZ is the yawing moment coefficient
 | Mesh 1 | Mach - 5% |  | Mach Baseline |  | Mach + 5% | 
 | Angle of Attack | 0 degrees | 6 degrees | 0 degrees | 6 degrees | 0 degrees | 6 degrees
Spalart-Allmaras | CL |  |  | -0.001168 | 0.054496 |  | 
 | CD |  |  | 0.040206 | 0.046212 |  | 
 | CMx |  |  | 0.000001 | 0.000004 |  | 
 | CMy |  |  | 0.030040 | -1.526265 |  | 
 | CMz |  |  | 0.002632 | 0.001183 |  | 
Shear Stress Transport | CL | 0.000428 | 0.069069 | 0.000564 | 0.067977 | 0.001171 | 0.066865
 | CD | 0.043195 | 0.049761 | 0.041294 | 0.047937 | 0.039244 | 0.046229
 | CMx | 0.000002 | 0.000005 | 0.000002 | 0.000005 | 0.000002 | 0.000005
 | CMy | -0.024661 | -2.069780 | -0.025681 | -2.016400 | -0.029003 | -1.964558
 | CMz | 0.007575 | -0.004533 | 0.005838 | -0.005253 | -0.000787 | -0.005864
 | Mesh 2 | Mach Baseline | 
 | Angle of Attack | 0 degrees | 6 degrees
Shear Stress Transport | CL | 0.000154 | 0.030719
 | CD | 0.037881 | 0.041893
 | CMx | 0.000001 | 0.000002
 | CMy | -0.004990 | -0.495014
 | CMz | -0.002349 | -0.000902
 | Mesh 4 | Mach Baseline | 
 | Angle of Attack | 0 degrees | 6 degrees
Shear Stress Transport | CL | 0.001522 | 0.067774
 | CD | 0.040540 | 0.048020
 | CMx | 0.000001 | 0.000005
 | CMy | -0.025546 | -2.008672
 | CMz | -0.004545 | -0.002233
 | Mesh 3 | Mach Baseline | 
 | Angle of Attack | 0 degrees | 6 degrees
Shear Stress Transport | CL | 0.001029 | 0.063555
 | CD | 0.039892 | 0.047398
 | CMx | 0.000002 | 0.000005
 | CMy | 0.001806 | -1.780981
 | CMz | -0.004219 | -0.002216
 | Mesh 5 | Mach Baseline | 
 | Angle of Attack | 0 degrees | 6 degrees
Shear Stress Transport | CL | -0.000028 | 0.063930
 | CD | 0.036864 | 0.039971
 | CMx | 0.000001 | 0.000003
 | CMy | 0.001062 | 0.681614
 | CMz | -0.000123 | 0.002436
Baseline Case Values

## Slide 20: Results
Uncertainty was calculated using the equations presented previously and is presented as a raw value and as a percentage of the baseline value for each coefficient
Total Uncertainty |  | 
 | 0 degrees | 6 degrees
CL | 2.75E-06 | 1.82E-04
CD | 4.16E-06 | 3.97E-06
CMx | 9.17E-13 | 9.17E-13
CMy | 2.85E-03 | 5.05E+00
CMz | 6.81E-05 | 3.80E-05
Normalized Uncertainty |  | 
 | 0 degrees | 6 degrees
CL | 0.49% | 0.27%
CD | 0.01% | 0.01%
CMx | 0.00% | 0.00%
CMy | 11.08% | 250.58%
CMz | 1.17% | 0.72%

## Slide 21: Results
The contribution from each input parameter was calculated from the total uncertainty and is presented as a percentage of the total uncertainty

## Slide 22: Results
6° configuration:

## Slide 23: CFD Wrapper
A preliminary wrapper was programmed in python to work with SU2
  Two scripts:
    First script takes in a configuration file for SU2 and a slurm file for the HPC
      Generates dataset and submits to HPC automatically
    Second script calculates uncertainties and outputs values in tabular format and charts as shown previously

## Slide 24: Future Directions and Conclusions

## Slide 25: Conclusions
Created a framework to calculate uncertainty in aerodynamic coefficients without the use of experimental data
Each input parameter contributed to the total uncertainty in some capacity
The highest uncertainty was seen in the pitching moment coefficient at 6° angle of attack
  Contribution was almost entirely from the mesh component
    Meshing is important and it will be worthwhile to spend more time getting higher quality meshes in the future
The contributions were different for the different configurations
Image from NASA
Notes: Now we have a hammer, got to find some nails

## Slide 26: Future Work
Create structured meshes for future test cases
Develop the wrapper to include more input parameters
Validate methodology against models where experimental data exists
Include numerical uncertainty in final value
Expand the input parameters to include others such as:
  Wall functions – on/off
  Surface roughness
  Additional boundary conditions – altitude, freestream pressure and temperature
Expand the output quantities of interest to include lineloads
  Primary quantity of interest in launch vehicle tests

## Slide 27: Acknowledgements
This work is supported by the NASA Launch Services Program via the Expendable Launch Vehicle Integrated Support (ELVIS) 3 contract, operated by a.i. solutions inc.
Thank you to Paul Schallhorn, Michael Harris, Michael Elmore, and Scott Clark
This research was supported in part through computational resources and services provided by the University of Arizona's Research Data Center (RDC)

## Slide 28: Questions/discussion
chanl.arizona.edu
stockdaleavery@arizona.edu
Hanquist@arizona.edu

## Slide 29: Backup slides