## Slide 1: Modeling Complex Cryogenic Tank Thermodynamics with Simple Spreadsheet Tools
Mark Wollen, IES
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Cryogenics Technical Session
Presented by: Mark A Wollen
Cryo1-03 Wed 11:10
& Course session Mon 3:30

## Slide 2: Modeling Complex Cryogenic Tank Thermodynamics with Simple Spreadsheet Tools
Mark Wollen, IES
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Cryogenics Technical Session
Presented by: Mark A Wollen
Not all that complex!
Nothing magic about cryogens
Applies to hot tanks (e.g. boilers) equally well

## Slide 3: Course Agenda
What do we want to get from a tank thermodynamics model? (5 min?)
Description of the thermodynamics problem (15 min?)
  Mass and energy balances, etc
  Understanding various thermal and mass diffusion coefficients, boiling models, etc.
Description and demonstration of the spreadsheet tool (15 min?)
  Simple tank fill, drain, effects of heat load, pressurization, vent, etc.
Modeling some trickier stuff (10 min?)
  Disturbance of tank contents – mixing, splashing, sloshing, quenching
  Bubbler pressurization theory (optional)
A hands-on demonstration (15-20 min?)
  Validating the tool with a coffee machine boiler
  Fee espresso to volunteers or those who answer the most questions right (time permitting)
Workbook and Excel Macro VBAs are Unrestricted*, Free Open Source Software – See me if you’d like a copy
* Gov’t personnel and civil servants responsible for assessing legal installation or use on gov’t furnished equipment

## Slide 4: What do we want from a tank thermodynamics model?
Tank conditions of interest
  Liquid conditions - saturated or subcooled
  Ullage gas in tank – may be hot or near liquid temperature, contains vapor phase as well as (possibly) a non-condensable pressurant gas
  Tank walls have non-trivial heat capacity (stored energy)
Operations of interest:
  Filling, draining, venting, pressurizing, heat load (to liquid and ullage)
  Disturbance to tank contents: 1) quenching of hot tank walls, 2) mixing of liquid and ullage
Things we want to quantify:
  Pressure rise rate due to heat load if tank locked up
  Pressurant gas needed to expel (and subcool) liquid
  Pressure excursions due to tank disturbances
  Other?

## Slide 5: Choosing an appropriate modeling approach
Model options
  Equilibrium liquid and ullage, or no liquid/ullage interaction (too simple)
  Full two-phase CFD simulation (exceedingly complex and computationally intensive)
  “Pancake” models (multiple vertical liquid, ullage, and tank-wall nodes)
Simplest model that captures all the physics to first order consists of 4 nodes:
  Single ullage node
  Single liquid node
  Wall node associated with ullage
  Wall node associated with liquid
The 4 node model is a “classic” approach, implemented in Fortran in 1960s - 70s, and probably prior to that with “human” computers
Great for understanding the critical physical principles at work, performing preliminary design studies, can be fairly accurate with proper “tuning”

## Slide 6
Some preliminaries - understanding nomenclature
M liq = Mass of liquid in tank
E liq = Energy of liquid in tank
T liq = Temperature of liquid in tank
Rho liq = Density of liquid (funct of T liq)
P liq vp = Liquid vapor pressure (function of T liq)
M vap = Mass of vapor phase in tank
E vap = Energy of vapor phase in tank
M gas = Mass of non-condensible gas in tank
E gas = Energy of non-condensible gas in tank
T ull = Temperature of ullage in tank
V tank = Volume of entire tank
V liq = Volume of tank occupied by liquid
V ull = Volume of tank occupied by gas
Typical Nomenclature:
Heat flow from ullage wall node to ullage node
Convection coeff for the ullage
Area for the ullage wall
Temperature of the ullage wall node
Temperature of the ullage node
When in plain text format, rather than equation format:
Note, typically:
  H, h – used for enthalpies, kW, kW/kg
  g – used for convection coefficient

## Slide 7
Tank Thermodynamics Modeling (liquid/ullage/wall node model)
+
Ullage CV boundary
Liquid CV boundary
Moving CV boundary
Note: Enclosed dashed regions show boundary flow or movement prior to incrementing time
Liquid vaporized and added to ullage due to bubbler:
Enthalpy added to liquid due :
Enthalpy leaving liquid to ullage due :
Enthalpy leaving liquid due to *:
Enthalpy entering ullage due to *:
* - Different due to different liquid and vapor energy reference levels
Venting:
Ullage pressurization relationships:
Liquid or two phase inflow:
Liquid outflow:
Liquid/vapor boundary mass and energy balance:
+
Supplemental heating:
Wall energies:
(PV work terms)

## Slide 8
Basic thermodynamic and tank equations
Work done by (or energy removed from) liquid due to change in liquid volume:
Work done by (or energy removed from) ullage due to change in ullage volume:
Volume relationships, and related PV work:
Primary thermodynamics relationships:
Normal boiling point for liquid
Ideal gas equations, with compressibility factor for the condensable vapor phase
Energy relationships assume constant specific heats and heat of vaporization
Liquid saturation pressure is function of temperature
Typically 2nd or 3rd order polynomial

## Slide 9
Wall heat transfer and thermodynamics modeling
Falling
Rising
Wall boundary mass and energy transfer:
Energy equations for wall nodes:
Heat transfer equations for wall nodes:
Where:
  g and k are wall convection coefficients and thermal conductivity
  L ~ ½ distance separating wall nodes (?)
  Ax = tank wall cross sectional area
Wall
Liquid

## Slide 10
Mass and energy Balance Relationships
Iterative mass balance relationships (5):
Iterative energy balance relationships (4):
Liquid:
Ullage (non-condensable gas):
Ullage (condensable vapor):
Liquid:
Ullage:
Tank wall regions (2):
Tank wall regions (2):
Basically, a big explicit time-iterative bookkeeping effort
  Explicit implies no sub-iterations – state at t+Dt is directly calculated from known conditions at t

## Slide 11
Selection of rate-governing coefficients
Successful use of the model depends on proper choices of the various convection, thermal and mass diffusion, and conduction coefficients that regulate the heat and mass transfer under various conditions
A few examples follow…

## Slide 12
Choosing an outer wall convection coefficient
External wall convection coefficient :
For free convection on a vertical cylinder, use, for example, Ref 1:
Nusselt number:
Grashof number:
Prandtl number:
Property eval temp:
For forced convection (wind) on a vertical cylinder:
For forced convection (ascent, moderate Mach) on a vertical cylinder:
If frost forms on outside of tank, creating insulating layer:
Can add insulation term, or knock down h:
Some classic Nusselt number correlations and results
Generally similar process and results for selecting reasonable convection coefficients inside tank
If trying to match a known operational tank or system, can “tune up” coefficients from data
Ref 1 – Holman, J.P., Heat Transfer

## Slide 13
Thermal and mass diffusion relationships at liquid-ullage interface
Thermal and mass diffusion relationships at liquid-vapor interface:
Boiling mass transfer relationship, liquid to ullage:
is thermal convection coefficient at surface, kW/m^2/K
is mass diffusion coefficient at surface, kg/s/m^2/K
is constant with units 1/s (“scaling” constant)
is constant with units 1/bar (“knee sharpness” constant)
Enthalpy leaving ullage due to *:
Enthalpy entering liquid due to *:
Enthalpy leaving liquid due to *:
Enthalpy entering ullage due to *:

## Slide 14
Choosing coefficients for mass diffusion at liquid-vapor surface
Where DM0 is mass diffusion coefficient in absence of non-condensable gas
This approach is highly empirical approximation, due to bulk properties nature of liquid and ullage, but it can work surprisingly well for condensation
  For evaporation, perhaps gas interference effect should be adjusted or turned off
Mass diffusion slowed by presence of non-condensable gas:
Mass diffusion assumed driven by difference between ullage vapor partial pressure and bulk liquid saturation pressure:
Typical value range for many fluids and calm surface:
If disturbed/fragmented surface
is possible (due to greatly enhanced surface area)

## Slide 15
Ullage heat transfer and stratification considerations
Heat flow into ullage (typical cryogenic tank)
Warm vapor rises to top
Convection inhibited
Cooled vapor sinks or condenses along wall
Heated (and added) vapor rises from liquid
Strong convection
Heat flow out of ullage (typical boiler tank)
In absence of venting, ullage gas rapidly stratifies and becomes (on average) much warmer than liquid
Ullage gas temperature tends to track liquid temperature
Liquid temp
Liquid temp
Vertical temp distribution
Vertical temp distribution
er values
Wall temp
Wall temp

## Slide 16
Explanation of boiling model
Exponential cutoff characteristic (penalty function)
Empirical boiling mass transfer relationship, liquid to ullage:
is constant with units 1/s (“scaling” constant)
is constant with units 1/bar (“knee sharpness” constant)
Objective is to capture basic boiling characteristics such that algorithm runs in a stable manner
Boiling rate is proportional to mass of liquid in tank
Negligible boiling if Psat < Pull
Rapid increase if Psat > Pull

## Slide 17
What about tank disturbances (Mixes and Quenches)
Mixing of liquid with ullage
  Liquid sprays or splashes into ullage
Consequence
  High heat and mass transfer between liquid and ullage
  Ullage and liquid reach equilibrium in limit
Quenching of walls
    Liquid sloshes or wicks up walls
Can explicitly solve equations for mix and quench limits, but…
  Easier to brute-force solutions by driving up appropriate convection, conduction, and diffusion coefficients
  This also provides some transient behavior modeling, if test data available to aid in coefficient selection
In real world, various combinations of these two events are likely to occur
Consequence
  High heat transfer between ullage wall and liquid
  Possible boiling
  Ullage walls quenched to liquid temperature in limit
Will usually drop tank pressure
Will usually raise tank pressure

## Slide 18
Description of spreadsheet tools
Implementation of 4 node model in spreadsheets with VBA macros

## Slide 19
Macros summary (1 of 2)
Six macros to drive analysis operations
  Move condition data to appropriate locations
  Increment analysis intervals and log data

## Slide 20
Macros summary (2 of 2)
Dedicated macros to set up for a “Mix” or “Quench” simulation
Equivalent to “Normal” setup, but using different modeling conditions

## Slide 21
Worksheets – Setup1
Work through Worksheets left to right
“Setup1” is for fluid selections and tank parameters

## Slide 22
Worksheets – Setup2
“Setup2” is for setting initial conditions, and initializing analysis

## Slide 23
Worksheets – SetupNorm
“SetupNorm” sets:
  Thermal and mass diffusion coefficients
  Gas and liquid flow control
  Supplemental heating
“SetupMix” and “SetupQuench” are essentially identical to “SetupNorm”

## Slide 24
Worksheets – Run
“Run” is where data is displayed and time step execution is controlled
Results of last analysis interval
Cumulative results (logged data)
Pressures
Temperatures
Masses
Mass flows

## Slide 25
Worksheets – TankThermoModel
This is the Worksheet where all the calculations occur
~ 80 columns
~ 1050 rows

## Slide 26
Worksheets – TankThermoModel
Row 1022 and on is where logged data is recorded
All masses, energies, temps, press, flows, etc logged at specified intervals (10 sec in this example)

## Slide 27
Analysis demonstration (optional)
Perform real time analysis demonstration of tank loading, pressurization, outflow with heating (i.e., ascent), and mix/quench disturbance for a hydrogen tank

## Slide 28
Example simulation – Hydrogen tank loading and press’n
Loading
Press’n
Loading, 1 kg/s
Press’n
He, 298 K
Heat leakage
He, 298 K

## Slide 29
Example simulation – Hydrogen tank outflow/ascent
Liquid evaporating into ullage as temperature rises
Cold liq wall being added to warm ull wall
Liquid outflow, 1.5 kg/s
MECO/undisturbed
Liquid outflow
MECO/undisturbed
H2 ullage press, 0.005 lbm/s, 350 R
Liq vap press rise
Due to env heating
1x
3x heating

## Slide 30
Example simulation – Hydrogen tank post-outflow MIX
Liquid saturates
MIX (liq-ullage mix)
MIX (liq-ullage mix)
Ullage chills
Liquid boils
~4 kg vap add’n to ull
Pressure collapses

## Slide 31
Example simulation – Hydrogen tank post-outflow QUENCH
Liquid saturates pressure spikes
QUENCH (Liquid quenches tank walls)
Ullage cools
Liquid boils
~7 kg vap add’n to ull
QUENCH (Liquid quenches tank walls)
Ullage wall chills

## Slide 32
Example simulation – Post-outflow MIX-QUENCH
Liquid saturates on mix, pressure spikes on quench
MIX
Liquid boils
~11 kg vap add’n to ull
QUENCH
Temps all approaching equilibrium
MIX
QUENCH
Question – What about a QUENCH-MIX rather than a MIX-QUENCH?

## Slide 33
Possible future enhancements and improvements
Lacks an ullage wall condensation model
  Generally not needed for cryogens, but would improve simulation for boilers
Time steps are fixed and manually set
  Automatic time step selection could speed up execution and avoid some initial work, but might add its own problems
Tank geometry and wall model refinements
  Currently simple cylindrical shape for area-volume-height
  Dynamically adjusting length scale for intra-wall heat transfer would improve wall conduction simulation
Lacks adsorption of non-condensable gas in liquid
  Can be of importance with hydrogen-helium or water-air combinations

## Slide 34
A practical example and algorithm validation
T
T
P
Pwr meter
Heat LOSS through walls
Heat addition
to liquid (950W)
Ullage vent (frother)
Liquid outflow (to coffee basket)
Ullage and liquid thermocouples
Ullage pressure
Espresso machine boiler
1 liter boiler
Stainless steel
2.2 kg boiler mass
Bare (chrome) walls
950 W heating element
Thermal control feedback

## Slide 35
Boiler through 200 seconds
Liquid evaporating into ullage as temperature rises
Approaching vent level
What’s going to happen when we vent?

## Slide 36
Boiler through 280 seconds
Ullage venting
Ullage venting
Non-condensable gas vented off
Boiling kicks-in as Pull drops to Psat
Tull perturbation due to venting
Approaching second venting – what’s going to happen now?

## Slide 37
Boiler through 420 seconds
Heater cycling
Ullage venting
Heater cycling
Ullage venting

## Slide 38
End of presentation
Questions?
Time for coffee break?