## Slide 1: Preliminary CFD Simulations of a Cryogenic Film Condensation Experiment
NASA Glenn Research Center
Fluid and Cryogenic Systems Branch (Code LTF)
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Cryogenics Technical Session
Presented by: Justin Pesich

## Slide 2: Outline
Motivation
CFM Model Validation Roadmap
Fundamental Film Condensation Experiment
STAR-CCM+ Fluid Film Model with Phase Change
Preliminary CFD Results
  Nusselt Theory, CFD, and Experiment
  Mesh independence
  Surface Tension
  Drag
References

## Slide 3: Motivation
In-Situ Resource Utilization (ISRU) is an enabling technology to maintain a sustainable presence on the Lunar and Martian surfaces
ISRU plants will require liquefaction technologies to accumulate cryogenic propellants for ascent vehicles (LOX, LCH4) or life support (LOX)
Liquefaction involves injecting gaseous propellant into a tank with active cooling to promote condensation
CFD models can be utilized to predict liquefaction rates of cryogens at various operating conditions and inform lower-fidelity nodal models that can predict the entire liquefaction process practically
Credit: NASA [1-2]
VIPER
Mars ISRU plant

## Slide 4: CFD Model Validation Roadmap
Fundamental Film Condensation Experiment
Cryogenic Fluid In-situ Liquefaction for Landers (CryoFILL)
  Brassboard and Prototype testing
  Nitrogen used as surrogate for Oxygen in Brassboard testing
  Oxygen liquefaction for Prototype testing
  Broad Area Cooling Neon loop
Ref [3]: Johnson et al., “Liquefaction of Cryogenic Fluids for Production and Storage of Commodities on Extra-Terrestrial Surfaces,” Space Cryogenics Workshop, 2021.
CryoFILL Prototype Tank

## Slide 5: Film Condensation Experiment: Overview
Combustion Research and Flow Technology Inc. (CRAFT Tech) and University of Connecticut (UCONN) have completed two separate Phase I SBIR contracts on Film Condensation experimentation and modeling (Ref. [4])
  July 2022 – Jan 2023 (80NSSC22PA988)
  Aug 2024 – Feb 2025 (80NSSC24PB292)
Phase II has been awarded for the most recent Phase I contract
SBIR Modeling Objectives:
  Develop accurate sub-grid CFD models for modeling condensation of cryogens
  Modeling framework shall capture growth and transport of liquid condensate while conserving mass, momentum, and energy
SBIR Experimental Objectives:
  Conduct fundamental film condensation experiments on a flat plate using Methane, Oxygen, and Nitrogen
  Obtain measurements of pressure, temperature, flow rate, and film thickness (optical)

## Slide 6: Film Condensation Experiment: Schematic
Credit: UCONN

## Slide 7: Film Condensation Experiment: Chamber and Test Plate
Visualization Chamber
Brass Test Plates
Oxygen test plate
Credit: UCONN

## Slide 8: Film Condensation Experiment: Film Thickness Measurement
Credit: UCONN

## Slide 9: Film Condensation Experiment: Front Visualization
Film Condensation: ~10K Subcooling
Dropwise Condensation: ~18K Subcooling
KEY FINDING: PLATE SUBCOOLING DIRECTLY AFFECTS MODE OF CONDENSATION
Credit: UCONN

## Slide 10: STAR-CCM+ Fluid Film Model with Phase Change
STAR-CCM+ [5] models thin liquid films on solid surfaces using a fluid film solver that computes a sub-grid film thickness for every boundary cell (1D solver)
Fluid film can grow or shrink via condensation or evaporation depending on the local conditions
Bulk vapor phase is not coupled to the fluid film through momentum equation
  Bulk vapor does not “see” fluid film
  However, a drag force term can be implemented so that pressure variations are accounted for in film shape
Piecewise linear temperature profile assumed through thickness of film:
Sub-Grid Film Evap/Cond Solution Procedure:
  Calculate interfacial heat flux on each side of film interface assuming interfacial temperature is equivalent to Tsat (Eqn 1)
  Calculate mass transfer rate (Eqn 2)
  Calculate rate of change of film thickness (Eqn 3)
Eqn 1
Eqn 2
Eqn 3
Source: Ref [5]
solid
film
Vapor BL

## Slide 11: Condensation on a Dry Wall
The solution procedure encounters issues when the CFD solution is initialized with zero film thickness (dry wall)
Heat transfer coefficient in the film is given by Eqn 4, where zero film thickness results in infinite condensation rate
By default, the sub-grid model assumes a minimal thickness of 10-8m, however this still predicts very high condensation rates
In reality, the onset of condensation is driven by droplets growing at nuclei, which eventually form a fully wetting film
Therefore, a limiter (Eqn 6) is applied to the calculated condensation rate for stability when to scale the interfacial area
Limiter is dependent on user-defined Minimum Nuclei Radius and Nucleation Density parameters
Eqn 4
Source: Ref [5]
Eqn 5
Eqn 6
Eqn 7
This procedure does not affect the steady state solution, only initial transient

## Slide 12: CFD Model Setup
Working fluid: Methane (CH4)
Compressible ideal gas + LCH4 film
  Temperature-dependent vapor properties
  Constant liquid film properties
Vapor phase coupled to fluid film via condensation and evaporation model
Laminar flow
3D Conjugate Heat Transfer
  Brass temperature-dependent properties
Surface Tension neglected
  Sensitivity study considered
Unsteady Δt = 0.05s
Run until steady state condition is achieved (constant liquefaction rate)
Mesh ~204k cells
Solid Brass
Fluid Domain
Condensing surface 22.6mm x 55.8mm

## Slide 13: Model Boundary Conditions
Ti,fluid = 292.1K
Ti,solid = 115K (slightly above saturation temp)
Condensing surface/film region
“Edge outlet” for film to flow off plate and track
Tbath = 77.4K
Vin = 0.5m/s
Tvapor,in = 292.1K
Pressure Outlet
Sym planes
14.7psia
q" = 0
q" = 0

## Slide 14: Preliminary CFD Results: Plate Temperatures
Downstream temperatures match reasonably well
Upstream and center temperature predictions are significantly under-predicted by 5-10K
Constant wall temperature set to LN2 bath temperature likely not accurate due to stratification and heat leak
T_i
T_s
T_plate
T_plate is solid metal surface temperature

## Slide 15: Preliminary CFD Results: Film Thickness
Film thickness likely over-predicted due to under-prediction of solid temperatures
% error = 222% (3x over-predicted)
Sub-grid model slightly out-performs Nusselt Theory [6]
Condensing surface 22.6mm x 55.8mm

## Slide 16: Preliminary CFD Results: Liquefaction Rate
Liquefaction rate leveling off indicates steady state condition
Integrated condensation rate and mass flow of film off plate boundaries are identical at steady state
Simulation took 1.2 hrs on 8 cores to complete 50s

## Slide 17: Mesh Independence
Baseline Mesh
0.5mm plate
Fine Mesh
0.2mm plate
~204k cells
~2.8M cells

## Slide 18: Effect of Surface Tension
Film solver yielded a large discontinuity when using a 0 degree contact angle
Solution for 2 degree contact angle identical to baseline case with no surface tension
STAR-CCM+ uses surface tension model by Brackbill et al. [7]
0deg Contact Angle
2deg Contact Angle

## Slide 19: Drag Force
The only way to “couple” the momentum of the vapor to the film is by applying a drag force:
CD = 0.27 (CFD predicted CD) and 1.5, 5, 50, 200 all yielded identical results to baseline case
CD = 500 caused large, dynamic ripples (unrealistic case)
CD = 500

## Slide 20: Conclusions and Discrepancy Investigations / Future Work
STAR-CCM+ fluid film model with phase change provides a robust CFD framework to predict film condensation for liquefaction applications
  Surface Tension model with 0 deg contact angle introduced instabilities, but is not necessary
  Drag force negligible for films on the order of 10 µm (not surprising)
Determine if over-prediction of film thickness is common between Methane, Nitrogen and Oxygen experiments
  Oxygen dataset contains multiple film thickness measurements along the length of the plate
  Determine sensitivity of film thickness to inlet vapor temperature
Over-simplified boundary conditions
  LN2 bath temperature
  Heat leaks into visualization chamber (Thermal Desktop model of entire chamber)
  If we force the internal plate temperatures to match the data, does CFD predict an accurate film thickness? If not, why?
Inquire on accuracy of measurement technique
  Error bars ±15 µm is on the same order as measurement (20-30 µm)
  Contractor reported plate torsion
  Horizontal plate film condensation experiment: larger film will provide more accurate measurement and drag study

## Slide 21: References
https://science.nasa.gov/mission/viper/
https://www.nasa.gov/overview-in-situ-resource-utilization/
Johnson, W. L., Dimston, A. E., Valenzuela, J. G., Kashani, A., Smith, J. W., Chan, H. M., Wendell, J. C., Stephens, J. R., Balasubramaniam, R., Johnson, K. P., and Miller, E. J., “Liquefaction of Cryogenic Fluids for Production and Storage of Commodities on Extra-Terrestrial Surfaces,” Space Cryogenics Workshop, 2021.
Pesich, J. M., “A Summary of Recent SBIR and STTR Projects in Support of Cryogenic Fluid Management Modeling,” TFAWS presentation, 2024.
Siemens Simcenter STAR-CCM+, Ver. 19.02.009-R8 (2402), Plano, TX, 2024.
Ghiaasiaan, S. M., Two-Phase Flow, Boiling, and Condensation, 2nd ed., Cambridge University Press, Cambridge, UK, 2017, Chap. 15, pp. 566–568.
Brackbill J. U., Kothe, D. B., Zemach, C., “A continuum method for modeling surface tension,” J. Comp. Phys. Vol. 100, 1992, pp. 335–354.

## Slide 22: backup

## Slide 23: Temperature Results thru Plate, Film, and Vapor

## Slide 24: Film Thickness and Condensation Rate

## Slide 25: Nusselt Theory for Film Condensation [5]
Assumptions:
  Steady state, laminar film flow
  Constant wall temperature
  Stagnant, pure, saturated vapor
  Zero shear stress at the film surface
  Constant-property condensate liquid
  Negligible liquid inertia
  Linear temperature profile across the condensate
Main Shortcomings:
  Does not account for subcooling of the condensate film
  Does not account for forced convection where shear stress at the film interface is significant
  Does not account for ripples or waves (Ref > 33) which cause mixing and enhances heat transfer
  ±50% accuracy

## Slide 26: Condensation on a Dry Wall cont.
Varying Film Thickness

## Slide 27: LN2 Bath
Credit: UCONN

## Slide 28: Film Thickness Measurement Location
Credit: UCONN