## Slide 1: Simulation of Time-Dependent Heat Transfer in Spherical Bubbles With Application to Bubble-Through Nuclear Thermal Rocket Engines
Dakota Santana D. Keith Hollingsworth Ph.D. Student Professor
Department of Mechanical and Aerospace Engineering
The University of Alabama in Huntsville
POC: Dakota, djs0057@uah.edu

## Slide 2: Bubble-Through Liquid Nuclear Thermal Rocket
(Rom, 1968)
History
Proposed in 1954 by McCarthy
Theorized Specific Impulse 50 – 100% greater than solid cores
Sporadically studied since with recent design effort referred to as Centrifugal Nuclear Thermal Rocket (CNTR)
Operations
Fissile liquid produces a nuclear hear source
Centrifuge contains the liquid
Bubbles radially inward cooling the centrifuge and heating up in the liquid
H2
U + Refractory
4000 K < T < 6000 K
Isp ~ 1200 – 1800 s

## Slide 3: Bubble Conditions As Predicted by Engineering Model* *Keese and Hollingsworth, 2022
Rapidly Changing Bubble Conditions
Hydrogen Dissociation →
  Conductivity and volumetric specific heat of gas approaches the liquid within 1 order of magnitude
Thermal Gradient →
  Marangoni numbers up to 6000 predict surface tension induced advection
  Gas Material Properties may vary up to 50% from top to bottom of bubble
  Time dependent thermal boundary condition on the bubble
Morphology →
  Impact of rapid expansion
T = 3228 K, g = 1528
T = 2935 K, g = 1547
T ~ 2981 K
u = 2.47 m/s
r = 0.39 mm
Size Change to Scale
T = 4887 K, g = 1151
T = 4868 K, g = 1175
T ~ 4870 K
u = 2.45 m/s
r = 0.51 mm (2.4x Vol)
2.9ms

## Slide 4: Exploration Space
Clift et. al., 1978
Colombet et. al., 2013
Juncu, 2010
Saboni, 2016
Wadewitz and Specht, 2001
Predicted Analytical
Traditional Heat/Mass Transfer models assume:
Bubble → Liquid (min Nu, Sh = 2)
Liquid → Bubble (min Nu, Sh = 6.58) [shown in graph]
Choice dictated by rate-limited phase
Validation Framework and Respective Challenges
Low Re:
Resolving bubble interface (reference cases have fixed interface)
Pulling and processing data
High Re:
Spurious currents from low Capillary numbers
3D LES capability
Spheroid:
Alternative bubble shape
Required step for stable spherical cap bubble
High Re
Low Re
Spheroid

## Slide 5: CFD Setup
Ansys Fluent, 2D Axisymmetric, VOF
Lagrangian grid, Eulerian solver:
Velocity predicted by Dijkhuizen equation
Maintain bubble in highly refined zone
Time Step:
Nusselt Number Calculations:
SIMPLE and PRESTO! were most commonly used schemes
Res ~ r/40 – r/80
r = Bubble Radius
Res/2
Res/4
Res/8
Pressure Outlet
Pressure Outlet
Inlet
Roughly to Scale
Structured Quad Grid + Tri Transitions

## Slide 6: Preliminary Investigation
Mean Velocity Error < 1.5%
Pe = 160
Non-Dimensionals |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Non-Dimensionals |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
(Colombet, 2013)

## Slide 7: Capacitance Factor Correction
Capacitance Based
Volume Based
 | Pe = 160 |  | Pe = 80 | 
 | Cap | Vol | Cap | Vol
 | 2.2e-4 |  |  | 
 | Pe = 160 |  | Pe = 80 | 
 | Cap | Vol | Cap | Vol
 | 2.2e-4 |  |  | 

## Slide 8: Noise Investigation
VOF strong at conserving mass
Noise in volume radius is unbiased → inconclusive
Capacitance Fraction changes cell weighting and turns the volume noise into clear capacitance radius walk
Extrema in correlate with Nusselt curve spikes
Expect reduced significance in 3D simulations as more cells represents the interface to average out noise
Spikes in Nusselt curves
Continuous
Persist through filtering
Investigate change in change in radius:
Liquid
Gas
Liquid
Gas

## Slide 9: Shortcoming of Capacitance Factor
Capacitance Averaging does not replace Volume Averaging
Capacitance weighting downplays behavior at outer edges

## Slide 10: Different Surface Reconstructions
PLIC
CICSAM
HRIC
Non-Dimensionals |  |  | 
Time step increased 25% Size Domain decreased 33% |  |  | 
Two step data filtering added: Small stencil Lowess Larger stencil 3rd order Savitzky-Golay |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Non-Dimensionals |  |  | 
Time step increased 25% Size Domain decreased 33% |  |  | 
Two step data filtering added: Small stencil Lowess Larger stencil 3rd order Savitzky-Golay |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Compressive

## Slide 11: High Reynolds Number
Predicted Velocity Error ~ 6%
(interfacial behavior maybe overly suppressed)
Non-Dimensionals |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Non-Dimensionals |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
(Saboni, 2016)

## Slide 12: Uranium Case
Non-Dimensionals Nominal |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Non-Dimensionals Nominal |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Liquid Uranium + Gaseous Hydrogen
4000 K, 100 atm, 2000 gs

## Slide 13: Conclusion
In VoF different definitions of fluid interface exist:
Volume based: best for momentum
Capacitance based: best for thermal
  Improves correlation to idealized models
  Viable analytical tool
Future Work:
High Re validation
ratio impact
VoF Interface
Capacitance Interface

## Slide 14: References
R. Clift, J. Grace, M. Weber, Bubles Drops and Particles, Academic Press, San Diego, 1978
D. Colombet et. al., “Mass or heat transfer inside a spherical gas bubble at low to moderate Reynolds number,” International Journal of Heat and Mass Transfer, 2013
Dijkhuizen,W.; Roghair, I.; Annaland, M.V.S.; Kuipers, J. DNS of gas bubbles behaviour using an improved 3D front tracking model—Drag force on isolated bubbles and comparison with experiments. Chem. Eng. Sci. 2010, 65, 1415–1426.
G. Juncu, “A numerical study of the unsteady heat/mass transfer inside a circulating sphere,” International Journal of Heat and Mass Transfer, 2010
J. Keese and K. Hollingsworth, "One-Dimensional Steady-State Thermal Model of CNTP Reactor," Nuclear Technology, 2023.
F. E. Rom, “Nuclear-Rocket Propulsion,” NASA TM X-1685, NASA, Nov. 1968
A. Saboni, “Mass transfer into a spherical bubble,” Chemical Engineering Science, 2016
A. Wadewitz and E. Specht, “Limit value of the Nusselt number for particles of different shape,” International Journal of Heat and Mass Transfer, 2001

## Slide 15: Error Investigation
Correlates to the island, mean radius calculated from this area is ~80% greater

## Slide 16: Uranium Case
Non-Dimensionals Nominal |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Non-Dimensionals Nominal |  |  | 
Fluid properties selected to replicated the key nondimensional in validating papers |  |  | 
Liquid Uranium + Gaseous Hydrogen
4000 K, 100 atm, 2000 gs
Pure Diffusion
No Convection
Finite Difference Model