## Slide 1: Atmospheric Waves Experiment (AWE) Thermal Control System: from Design through On-Orbit Thermal Performance
Mike Holt, Matt Ralphs
Space Dynamics Laboratory
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Thermal Control & Protection Technical Session
Presented by: Mike Holt

## Slide 2: Outline
Introduction to AWE
Thermal Control System Overview
Thermal Models
Thermal Testing & Model Correlation
On-Orbit Performance
Conclusions
https://stockcake.com/s?q=sign%20post%20crossroads; Free, royalty free

## Slide 3: Introduction to AWE (1 of 2)
Atmospheric Waves Experiment (AWE) provides the first global characterization of atmospheric waves (https://www.awemission.org/)
The Space Dynamics Laboratory (SDL) in Logan, Utah was selected to execute AWE as a Class D mission of opportunity in NASA’s Science Mission Directorate, Heliophysics Division.
Measures the dynamics and structure of global mesospheric gravity waves near the mesopause region of the atmosphere
Several ground-based Mesospheric Temperature Mappers (MTM) have been used, but AWE is the first space-based MTM.
Installed on the international space station (ISS) ELC 1 Site 3 since November 2023

## Slide 4: Introduction to AWE (2 of 2)
AWE is a suite of four wide field-of-view near-infrared cameras.

## Slide 5: Outline
Introduction to AWE
Thermal Control System Overview
Thermal Models
Thermal Testing & Model Correlation
On-Orbit Performance
Conclusions
https://stockcake.com/s?q=sign%20post%20crossroads; Free, royalty free

## Slide 6: Thermal Control System Overview (1 of 3)
Optomechanical Assembly (OMA)
  Houses the telescopes, filter wheel, detectors
  Dedicated, bi-directional radiator
Instrument Electronics Box (IEB)
  Five electronics boards
  Dedicated bi-directional radiator
ExPRESS Payload Adapter (ExPA)
  Allows for power and data connections between the payload and the ISS

## Slide 7: Thermal Control System Overview (2 of 3)
Bi-directional Radiators
  Maintain an unobstructed view to space
Four Detectors with independent TEC closed-loop control
  Continuously control the FPA to −30°C, heating and cooling
Copper thermal hub and conductor bar
  Good conductance to radiator with added thermal mass to survive unpowered robotic transfer
Four Pyrolytic Graphite Sheet (PGS) thermal straps
  Excellent vibration isolation and volume-specific thermal conductivity
  1.6 W/K, 52 grams, each

## Slide 8: Thermal Control System Overview (3 of 3)

## Slide 9: Thermal Control System Overview: Environment
Designed for two launch vehicles
Launched on CRS-29 aboard SpX Dragon Cargo

## Slide 10: Outline
Introduction to AWE
Thermal Control System Overview
Thermal Models
Thermal Testing & Model Correlation
On-Orbit Performance
Conclusions
https://stockcake.com/s?q=sign%20post%20crossroads; Free, royalty free

## Slide 11: Thermal Models: Overview
Thermal Desktop Models:
Official thermal models
Accurate snapshots of predicted payload temperatures
Includes ISS and launch vehicle interactions
Used to verify requirements
Underwent several correlations to test data
MATLAB Model:
Analytical model that only includes nodes for baffle and OMA radiator
Quickly evaluate the impact of changing environmental loads
Predict temperatures into the future with forecast environments
Baffle
OMA Radiator

## Slide 12: Thermal Models: Thermal Desktop
Thermal models include:
  AWE instrument developed by SDL
  ExPA provided by Boeing PTCS-ISS
  ISS provided by Boeing PTCS-ISS
  Launch vehicles provided by Boeing PTCS-ISS
ISS/AWE payload integrated thermal model takes ~8 hours to run each transient case
SpX Dragon Cargo
Dream Chaser Cargo
ExPA
ISS
AWE Instrument

## Slide 13: Thermal Models: MATLAB
Based on Steven L. Rickman’s course, “Introduction to On-Orbit Thermal Environments” from the 2014 Thermal and Fluids Analysis Workshop (TFAWS)
Uses a six-sided box and calculates environmental heat loads
  Includes two surfaces that are conductively connected
Baffle
OMA Radiator

## Slide 14: Outline
Introduction to AWE
Thermal Control System Overview
Thermal Models
Thermal Testing & Model Correlation
On-Orbit Performance
Conclusions
https://stockcake.com/s?q=sign%20post%20crossroads; Free, royalty free

## Slide 15: Thermal Testing and Model Correlation
AWE payload Thermal Desktop models were correlated to multiple thermal vacuum tests
Per NASA direction, the ExPRESS Payload Adapter (ExPA) was not included in the thermal vacuum tests
  The final flight configuration could not be fully simulated in thermal testing

## Slide 16: Outline
Introduction to AWE
Thermal Control System Overview
Thermal Models
Thermal Testing & Model Correlation
On-Orbit Performance
Conclusions
https://stockcake.com/s?q=sign%20post%20crossroads; Free, royalty free

## Slide 17: On-Orbit Performance: First Light
Temperatures were well within allowable flight temperature (AFT) limits
Operational temperatures are also well within predicted range
  Instrument temperatures vary ~3 ° C over an orbit
Detectors cooled to −30 ° C and very stable

## Slide 18: On-Orbit Performance: MATLAB Correlation to Telemetry & Forecasts
Comparison of thermal model predictions with the payload and ISS telemetry shows good agreement overall:
  Model predicted temperatures were within 3°C for beta 0 °, but only within 10 ° C for more extreme negative beta angles
Matlab models correlated to ~8 months of telemetry allows for continued forecasting of AWE payload thermal performance
  Most significant change was adjusting the environmental heat loads (vs beta angle) to better account for ISS interactions

## Slide 19: On-Orbit Performance: Year-Over-Year Telemetry (1 of 2)
Minimal performance changes year-over-year for the AWE thermal control system
  TEC performance is consistent
  No perceptible degradation in thermal control surfaces (radiators, baffle)
Differences in telemetry data are typically caused by ISS attitude changes or TEC setpoint changes
5-14 July 2025 ISS 180° Yaw Flip
Year 1: TEC Setpoint Changed to −25°C
discussed on next slide

## Slide 20: On-Orbit Performance: Year-Over-Year Telemetry (2 of 2)
Small spikes in temperature data are caused by small ISS attitude changes (visible in figures on right)
Small temperature differences at low beta angles are still under investigation
20
5-14 July 2025 ISS 180° Yaw Flip
Year 1: TEC Setpoint Changed to −25°C
circled below

## Slide 21: On-Orbit Performance: Lessons Learned
ISS attitude is adjusted regularly, often without prior notification (example at right)
  Primarily ISS pitch and solar panel orientation
  Payloads with a view of the solar panels and other ISS structures can see a large impact from these adjustments
ExPA temperatures were farthest from model predicted temperatures
  Wasn’t a huge surprise as NASA didn’t allow the ExPA to be included in the thermal testing
  Missed opportunity: should have taken emissivity measurements of the ExPA surfaces to compare against thermal model values
During TVAC testing, it was helpful to have a second temperature sensor (of a different type) placed near the flight sensors to provide insight into temperature sensor bias
  Flight ISS analog sensors (2-wire measurement, per ISS requirements) appear to have 2–3 ° C bias
Correlating to multiple sets of thermal test data throughout the program resulted in good predictions and few surprises on-orbit

## Slide 22: Outline
Introduction to AWE
Thermal Control System Overview
Thermal Models
Thermal Testing & Model Correlation
On-Orbit Performance
Conclusions
https://stockcake.com/s?q=sign%20post%20crossroads; Free, royalty free

## Slide 23: Conclusions
AWE thermal control system is performing as expected
  Payload temperatures have been continually maintained within predicted operational range
  Year-over-year results show consistent instrument performance
Test-correlation efforts were successful at reducing errors in thermal model performance predictions
  Stringent target correlation criteria and stability goals were met or exceeded during thermal testing
Telemetry-correlated MATLAB thermal model allows for forecasting payload thermal performance
On-orbit thermal performance of the AWE payload has been excellent!

## Slide 24
Questions?

## Slide 25: TFAWS 2025 Thermal Control & Protection Technical Session
Backup Charts

## Slide 26: BACKUP Thermal Model Correlations (1 of 2)
Project budgeted 5 °C of modeling analysis uncertainty
When determining the target correlation criteria, we accounted for three primary sources of uncertainty:
  Temperature sensor uncertainty
  Temperature and heater power stability
  Model correlation accuracy
Target criteria were met or exceeded for all balance points
Thermal Balance Stability Goals and Achieved Values
Model Correlation Criteria

## Slide 27: BACKUP Thermal Model Correlations (2 of 2)
Final flight instrument thermal vacuum testing included four distinct thermal balance points for model correlations.
Thermal model changes during final flight model correlation that most significantly affected the temperature and heat flow results were:
  MLI e*
  GSE connections to the hardware (joint conductance)
  Wiring harness conductances
  Note: previous TVAC tests helped to refine AWE instrument internal parameters.
Highest areas of outstanding uncertainty are related to the connections between AWE instrument and ExPA
  Conductances based on calculated estimates instead of test measured values

## Slide 28: BACKUP On-Orbit Performance: Year-Over-Year Telemetry