## Slide 1: Novel Pulsating Heat Pipes Featuring Fractals for Performance Enhancement
Dr. Zishan Akhter & Prof. Phillip Hart
Renewable and Sustainable Energy Research Center, Technology Innovation Institute (TII)
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Thermal Control & Protection Technical Session
Presented by: Dr. Zishan Akhter

## Slide 2: Introduction: PHP
Pulsating heat pipes (PHPs) are passive thermal management devices.
Wickless and capillary-driven, relying on pressure oscillations from evaporation/condensation cycles
Slug–plug vapor–liquid flow enables efficient two-phase heat transfer in serpentine or looped channels
Configurations: single-loop, multi-loop, flat-plate, embedded, and miniaturized (mPHPs)
Miniature PHPs (mPHPs): High surface-to-volume ratio resulting in faster thermal response and compact integration
Ideal for low-power thermal control in electronics, CubeSats, avionics, power modules, and fuel cells
Key performance factors: surface wettability, nucleation dynamics, fluid properties, flow regime stability
Scalable, lightweight solution for harsh environments — microgravity, vacuum, and constrained volumes

## Slide 3: Introduction: Fractals
Fractals are self-similar, scale-invariant structures observed in both nature and mathematics
Enable multi-scale surface engineering for enhanced transport phenomena in fluids and heat transfer
In thermofluid systems, fractal textures increase wetted surface area and induce flow disturbances
Enhance phase-change heat transfer by promoting liquid film thinning, nucleation, and vapor transport
In this study, fractal wall textures are integrated into mPHPs to improve thermal response and performance
Koch snowflake
Heighway Dragon
Sierpiński carpet
Hilbert curve

## Slide 4: Fractal Selection
Koch snowflake: sharp edge density and high perimeter-to-area ratio enhance evaporation and thin-film formation
Sierpiński carpet: hierarchical porosity supports multi-scale nucleation site distribution and vapor-liquid separation
Heighway Dragon: curved, asymmetric contours induce localized vortices and directional flow confinement
Hilbert curve: space-filling, self-avoiding path ensures maximized wall-fluid contact with high geometric symmetry
Koch (order-1)
Drgn (order-4)
Srpk (order-2)
Hlbt (order-3)

## Slide 5: mPHP Design
Ø 5 mm
Ø 3 mm
5.5 mm
5.5 mm
25 mm
Evaporator
Condenser
Adiabatic zone
1 mm
1 mm
Gravity (-Y axis)

## Slide 6: Fractal Integration
PHP-Design modification
Koch
Drgn
Srpk
Hlbt
Design features | Smth | Koch | Srpk | Hlbt | Drgn
Surface Area () | 71.13 | 78.27 | 80.46 | 80.79 | 77.07
Relative Increment |  | 10.04% | 13.12% | 13.58% | 8.35%
Volume () | 17.28 | 17.60 | 18.06 | 17.78 | 17.59
Relative Increment |  | 1.87% | 4.53% | 2.87% | 1.77%
Surface/Volume Ratio | 4.12 | 4.45 | 4.46 | 4.54 | 4.38
Relative Increment |  | 8.01% | 8.25% | 10.19% | 6.31%
Design features | Smth | Koch | Srpk | Hlbt | Drgn
 | 71.13 | 78.27 | 80.46 | 80.79 | 77.07
Relative Increment |  | 10.04% | 13.12% | 13.58% | 8.35%
 | 17.28 | 17.60 | 18.06 | 17.78 | 17.59
Relative Increment |  | 1.87% | 4.53% | 2.87% | 1.77%
Surface/Volume Ratio | 4.12 | 4.45 | 4.46 | 4.54 | 4.38
Relative Increment |  | 8.01% | 8.25% | 10.19% | 6.31%
Fractals grooved (0.1 mm) in curved zones
Surface area increased with minimal volume gain
Surface-to-volume ratio increased by ~10%

## Slide 7: Setup & Modelling
Working fluid: Ethanol
Saturation temperature: 351 K
Fill ratio: 50% (by volume)
Wall temperatures: Evaporator at 391 K, Condenser at 303 K
Wall condition: No-slip, no-penetration
Fluid–wall contact angle: 90° (neutral wetting)
Figure: Close-up of the structured hexahedral mesh used in PHP modelling
Material Setup & BC
CFD Modelling
Multiphase VOF model
Time step = 0.01-0.1 ms
Global average CFL maintained at ~1
Momentum model includes surface tension force

## Slide 8: Grid Sensitivity
Grid Features | Grid 1 | Grid 2 | Grid 3
Max Cell Size | 0.09 mm | 0.06 mm | 0.04 mm
Min Cell Size | 7.5 µm | 5.0 µm | 3.3 µm
Total Cell Count | 182,400 | 554,829 | 1,806,250
Orthogonal Quality (avg/min) | 0.95/0.59 | 0.95/0.59 | 0.95/0.59
Skewness (avg/max) | 0.06/0.6 | 0.06/0.6 | 0.06/0.6
Aspect Ratio (max) | 3.65 | 3.78 | 3.85
Vapor Fraction (evaporator) | Grid 1 | Grid 2 | Grid 3
Mean ( | 0.456 | 0.523 | 0.528
Relative Deviation | - | 14.69% | 0.09%
Median ( | 0.497 | 0.620 | 0.640
Relative Deviation | - | 24.7% | 3.22%
Vapor Fraction (evaporator) | Grid 1 | Grid 2 | Grid 3
 | 0.456 | 0.523 | 0.528
Relative Deviation | - | 14.69% | 0.09%
 | 0.497 | 0.620 | 0.640
Relative Deviation | - | 24.7% | 3.22%

## Slide 9: CFD Validation
Wall Heat Flux
Heat Flux (q’’) | Mean () | Median ()
Singh & Das (2024) | 49053.93 | 50256.19
Current CFD | 47728.43 | 47252.48
Deviation | -2.71% | -5.98%
Heat Flux (q’’) |  | 
Singh & Das (2024) | 49053.93 | 50256.19
Current CFD | 47728.43 | 47252.48
Deviation | -2.71% | -5.98%
Time-averaged results align with published data
Mean and median deviations within ±6%
Captures transient, two-phase thermo-fluid behavior
Resolves oscillatory flow and phase-change dynamics
Figure: Transient wall heat flux under steady PHP operation
Reference: Singh & Das, Appl. Therm. Eng., 2024, https://doi.org/10.1016/j.applthermaleng.2024.124388

## Slide 10: Results: Inception Stage
Figure: Temporal evolution of the area-weighted wall heat flux for different PHPs during inception stage
Wall Heat Flux
Fractals show higher initial 𝑞′′ from early nucleation
Heat flux drops sharply as vapor forms and insulates wall
Koch, Srpk and Drgn sustain 𝑞′′ via quick vapor detachment
Smooth PHP lags due to delayed wall wetting
Median 𝑞′′ increased by ~ 9-56% for fractals
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 56322.7 | 76891.0 | 69218.2 | 85888.9 | 75225.7
Δ (%) |  | 36.5% | 22.9% | 52.5% | 33.6%
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 56322.7 | 76891.0 | 69218.2 | 85888.9 | 75225.7
Δ (%) |  | 36.5% | 22.9% | 52.5% | 33.6%

## Slide 11: Results: Inception Stage
Vapor Volume Fraction
Fractals accelerate vapor build-up via floor nucleation
All converge to ~ 0.75-0.85 as balance sets-in
Srpk and Hlbt ramp fastest due to distributed active sites
Smth lags: sidewall-only sites delay bubble initiation
Median increased by ~ 0.8-15% for fractals
Figure: Temporal evolution of the vapor volume fraction in evaporator for different PHPs during inception stage
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 0.52 | 0.61 | 0.56 | 0.55 | 0.60
Δ (%) |  | 16.1% | 6.8% | 5.2% | 14.2%
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 0.52 | 0.61 | 0.56 | 0.55 | 0.60
Δ (%) |  | 16.1% | 6.8% | 5.2% | 14.2%

## Slide 12: Results: Inception Stage
Characteristics:
Nucleation is random and unanchored, driven by stochastic superheat zones.
Bubble growth is nonuniform, causing uneven pressure wave generation.
Slugs fail to form early; instead, bubbles coalesce chaotically.
Cross-sectional vapor evolution reveals shallow penetration and unstable vapor bridges.
Delayed establishment of rhythmic plug–slug flow explains transient instability.
0.015 s
0.035 s
0.025 s
0.030 s
0.020 s
Bubble dynamics (Smth)

## Slide 13: Results: Inception Stage
Characteristics:
Nucleation initiates at groove tips due to localized superheat.
Bubble coalescence accelerates slug formation by 0.030 s.
3D vapor evolution shows deep phase bridging across cross-section.
Surface grooves guide bubble growth and stabilize phase transitions.
Faster plug symmetry supports early thermal loop activation.
0.015 s
0.035 s
0.025 s
0.030 s
0.020 s
Bubble dynamics (Koch)

## Slide 14: Results: Inception Stage
Characteristics:
Hierarchical grooves induce rapid nucleation at corners.
Bubble clusters grow anisotropically (circumferential) and merge laterally.
Delayed plug formation (~0.035 s) with irregular vapor shape.
Cross-section shows incomplete phase bridging till late.
Strong nucleation density drives q″ but hinders vapor uniformity.
0.015 s
0.035 s
0.025 s
0.030 s
0.020 s
Bubble dynamics (Srpk)

## Slide 15: Results: Inception Stage
0.81 s
0.85 s
0.83 s
0.84 s
0.82 s
Droplet dynamics (Smth)
Characteristics:
Discrete condensation initiates at random surface sites
Droplets remain pinned—minimal sliding observed
No wetting guidance—growth limited to isolated spots
Weak droplet motion correlates with low thermal transport

## Slide 16: Results: Inception Stage
0.22 s
0.26 s
0.24 s
0.25 s
0.23 s
Characteristics:
Koch grooves guide nucleation along patterned walls
Droplets elongate axially with rapid plug formation
Enhanced wall interaction boosts condensation rate
Structured grooves induce droplet shift and merging
Droplet dynamics (Koch)

## Slide 17: Results: Inception Stage
0.22 s
0.26 s
0.24 s
0.25 s
0.23 s
Characteristics:
Srpk nucleation aligned with self-similar wall voids
Dense square droplets show delayed plug merging
Stable coexistence of droplets and vapor films
Geometry sustains interfacial area, moderates axial flow
Droplet dynamics (Srpk)

## Slide 18: Results: Steady Stage
Wall Heat Flux
Figure: Temporal evolution of the area-weighted wall heat flux during quasi-steady operation
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 51654.1 | 70173.5 | 70722.2 | 64454.7 | 66281.4
Δ (%) |  | 35.9% | 36.9% | 24.8% | 28.3%
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 51654.1 | 70173.5 | 70722.2 | 64454.7 | 66281.4
Δ (%) |  | 35.9% | 36.9% | 24.8% | 28.3%
Fractals sustain high 𝑞′′ via stable phase cycling
Srpk, Koch enhance 𝑞′′ through vapor detachment, slug motion
Smth shows deeper flux dips from poor rewetting, weak coupling
Fractals narrow fluctuation bandwidth via rhythmic slug–plug flow
Loop stability achieved post 1.5 s as oscillations dampen
Median 𝑞′′ increased by ~ 8-38% for fractals

## Slide 19: Results: Steady Stage
Figure: Temporal evolution of the vapor volume fraction in evaporator during quasi-steady operation
Vapor Volume Fraction
Drgn, Hlbt retain more vapor via wall groove hold-up
Srpk, Koch reduce through faster condensation
Smth holds moderate vapor from sidewall-only nucleation
Fractals modulate slug–plug dynamics via vapor pocket tuning
Hlbt achieves optimal two-phase distribution across zone
Median vary between -19-28% for fractals
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 0.59 | 0.54 | 0.45 | 0.67 | 0.75
Δ (%) |  | -8.4% | -23.6% | 14.9% | 27.6%
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 0.59 | 0.54 | 0.45 | 0.67 | 0.75
Δ (%) |  | -8.4% | -23.6% | 14.9% | 27.6%

## Slide 20: Results: Steady Stage
Slug/Plug Dynamics (Evaporator)
Smth
Drgn
Srpk
Hlbt
Koch

## Slide 21: Results: Steady Stage
Slug/Plug Dynamics (Condenser)
Smth
Drgn
Srpk
Hlbt
Koch

## Slide 22: Results: Steady Stage
Thermal Resistance
Figure: Temporal evolution of the thermal resistance of PHPs during quasi-steady operation
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 0.00175 | 0.00128 | 0.00126 | 0.00137 | 0.00134
Δ (%) |  | 26.9% | 28.0% | 21.7% | 23.4%
 | Smth | Koch | Srpk | Drgn | Hlbt
Mean | 0.00175 | 0.00128 | 0.00126 | 0.00137 | 0.00134
Δ (%) |  | 26.9% | 28.0% | 21.7% | 23.4%
Fractals lower by 20–29% via stable phase cycling
Srpk & Koch achieve lowest through efficient vapor detachment
Smth shows high due to poor rewetting and loop disruption
Fractals stabilize via rhythmic slug–plug dynamics
Median drops by ~21–28% for fractals

## Slide 23: Conclusion
Fractal wall designs significantly enhanced PHP thermal performance in both inception and steady stages
Koch and Srpk enabled early plug formation and highest wall heat flux through sharp-edged nucleation guidance
Hilbert and Dragon patterns sustained vapor hold-up and delivered balanced two-phase transport with lower fluctuations
Smooth-wall PHP lagged in nucleation and flow activation, resulting in higher thermal resistance and weaker circulation
Fractals reduced thermal resistance by ~ 28% and increased heat flux ~ 56%, driven by improved phase interaction

## Slide 24: Future Research
Establish a benchtop experimental test rig to validate and extend numerical insights
Develop low-order modeling frameworks to simulate PHP dynamics with reduced computational cost
Adapt the rig for application-driven PHP development, targeting low-grade heat and passive cooling systems
Explore TPMS and bio-inspired geometries for enhanced control over phase distribution and wettability
Explore integrated design strategies for sustainable thermal management in microelectronics and building envelopes

## Slide 25: Q&A Session
Dr. Zishan Akhter
zishan.akhter@tii.ae
Renewable and Sustainable Energy Research Center (RSERC)
Technology Innovation Institute (TII)
Abu Dhabi, UAE

## Slide 27: Supplementary Data

## Slide 28: Supplementary Data