## Slide 1
Characterization of Pulsating Heat Pipes for cooling detector planes and phased array antennas
Marcin Wójcik (KP Labs)
Artur Jurkowski (KP Labs)
Sławomir Pietrowicz (WUST)
Przemysław Kołakowski (Adaptronica)
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025

## Slide 2
Data processing electronics for space missions
About us
Gliwice, Poland
Established in 2016
80+ team members
2300m2 of private R&D facility
10+ missions & 35+ completed projects

## Slide 3
Agenda
Project overview
Approach
Test campaign
Thermal results
Microvibration results
Summary

## Slide 4
OUR PRODUCTS
SMART MISSION ECOSYSTEM
Project overview
MITIGATE

## Slide 5
Motivation
Project objectives
Manufacturing a set of PHP breadboards with various design features
Thermal characterization of breadboards
Characterization of microvibration disturbances
Consortium
KP Labs
Wrocław University of Science and Technology
Adaptronica
Potential applications
Detector plane cooling
Phased array antenna
MITIGATE project - Micro-g dIsturbance characTerizatIon and mitiGAtion in pulsaTing hEat pipes
This project is carried out for the European Space Agency as a part of TDE programme.
NASA
Wang, Y. et al. 2020
ESA
Research hypothesis

## Slide 6
OUR PRODUCTS
SMART MISSION ECOSYSTEM
Our approach
MITIGATE

## Slide 7
900x300mm (35.4x11.8 in)
Power transported: 200 W
Operational temperature -20°C to 65 °C (-4°F to 149°F)
1 row of loops
Breadboards
Small breadboards
Large breadboards
300x100mm (11.8x3.8 in)
Power transported: 30 W
Operational temperature -20°C to 45°C (-4°F to 113°F)
2 rows of loops
Technology baseline
Tubular PHP
  manufacturing simplicity
  scalability
  experience
Sandwich structure
Transparent section
Working fluid: methanol/acetone
Coper tubes
Interface material
Aluminum block
Aluminum cover

## Slide 8
Breadboard versions
Design features
Internal diameter: 1.5 mm vs 2.5 mm
Number of turns: 10 vs 14 turns
Working fluid: methanol vs acetone
Interface: epoxy vs soldering
Breadboards | size​ | Internal diameter​ | Number of​ loops​ | Working ​ fluid​ | Interface​
CHBB_L1_M​ | Large​ | 1.5​ | 14​ | Methanol ​ | Epoxy
CHBB_L1_A​ | Large​ | 1.5​ | 14​ | Acetone​ | Epoxy​
CHBB_L2_M​ | Large​ | 1.5​ | 10​ | Methanol ​ | Epoxy
CHBB_L3_M​ | Large​ | 2.5​ | 14​ | Methanol ​ | Epoxy
CHBB_L3_A​ | Large​ | 2.5​ | 14​ | Acetone​ | Epoxy
CHBB_S1_M​ | Small​ | 1.5​ | 14​ | Methanol ​ | Epoxy
CHBB_S2_M​ | Small​ | 1.5​ | 10​ | Methanol ​ | Epoxy
CHBB_S3_M​ | Small​ | 1.5​ | 14​ | Methanol ​ | Soldered​
CHBB_S3_A​ | Small​ | 1.5​ | 14​ | Acetone​ | Soldered​
Study of the impact on performance

## Slide 9
OUR PRODUCTS
SMART MISSION ECOSYSTEM
Test campaign
MITIGATE

## Slide 10
Test campaign
Filling ratio optimization test
Thermal performance test
Microvibration test
Horizontal Orientation
FR From 10% to 80%
Horizontal Orientation/Vertical (BHM&THM)
Optimal FR
Horizontal Orientation/Vertical (BHM&THM)
Optimal FR
30/50 ˚C
(86/122 ˚F)
30/45 ˚C
(86/113 ˚F)
Hor: 100/150/200 W
BHM/THM: 200W
Hor: 10/20/30 W
BHM/THM: 30W
65˚C (149˚F)
45˚C (113˚F)
SMALL
100/200 W
10/20/30 W
-20/10/30/50/65˚C (-4/50/86/122/149 ˚F)
-20/10/30/45 ˚C (-4/50/86/113 ˚F)
100/150/200 W
10/20/30 W
LARGE
SMALL
LARGE
SMALL
LARGE
Condenser temperatures
Power levels

## Slide 11
+
-
Power supply
Kapton heater
Chiller
DAQ
DAQ
Pressure sensor
Thermal test stand

## Slide 12
OUR PRODUCTS
SMART MISSION ECOSYSTEM
Results
MITIGATE

## Slide 13
Filling ratio test
Breadboards | Optimal Filling ratio
CHBB_L1_M​ | 30%
CHBB_L1_A​ | -
CHBB_L2_M​ | 20%
CHBB_L3_M​ | 30%​
CHBB_L3_A​ | 25%
CHBB_S1_M​ | 15%
CHBB_S2_M​ | 30%
CHBB_S3_M​ | 15%
CHBB_S3_A​ | 15%
Optimal FR selected based on
  the performance across all tested power levels
  operation stability
  in case of similar performance, the higher FR was selected
Obtained very low filling ratios for all small and large breadboards
Promising thermal performance
Results

## Slide 14
Thermal performance
Performance @max power: 200W / 30W Thermal resistance [˚C/W] |  |  |  |  |  | 
BB | Design parameter | -20˚C (-4˚F) | 10˚C (50˚F) | 30˚C (86˚F) | 50˚C (122˚F) | 45 / 65˚C (113/149˚F)
For large breadboards methanol exhibited better performance by
  achieving lower thermal resistance
  wider operational temperature range
For smaller breadboard acetone gave worse thermal resistance, but it operated in wider temperature range.
The soldered solution exhibited a reduced thermal resistance.
The 14-loop configuration demonstrated better thermal performance in all tested orientations.
Wider operational temperature range for larger diameter
CHBB_L3_M | Methanol | N/A | 0.077 | 0.033 | 0.027 | 0.025
CHBB_L3_A | Acetone | - | N/A | N/A | 0.066 | 0.027
CHBB_S3_M | Methanol | N/A | 0.315 | 0.152 | - | 0.123
CHBB_S3_A | Acetone | 1.540 | 0.212 | 0.183 | - | 0.164
CHBB_S1_M | Epoxy | N/A | 0.467 | 0.172 | - | 0.15
CHBB_S3_M | Soldered | N/A | 0.315 | 0.152 | - | 0.123
CHBB_S1_M | 14 turns | N/A | 0.467 | 0.172 | - | 0.15
CHBB_S2_M | 10 turns | N/A | 0.436 | 0.199 | - | 0.174
CHBB_L3_M | 2.5 mm | N/A | 0.077 | 0.033 | 0.027 | 0.025
CHBB_L1_M | 1.5 mm | - | - | N/A | 0.039 | 0.034
– not tested
N/A overheating
Working fluid
TURNS
DIAMETER
INTERFACE

## Slide 15
Thermal performance
Thermal resistance ˚C/W |  |  |  |  |  | 
Mode | Orientation | Horizontal |  |  | BHM | THM
 | Heater power | 200W | 150W | 100W | 200W | 200W
Step-up | 65˚C (149 ˚F) | 0.025 | 0.025 | 0.025 | N/A | N/A
 | 50˚C (122 ˚F) | 0.027 | 0.027 | 0.035 | 0.034 | 0.231
 | 30˚C (86 ˚F) | 0.033 | 0.035 | 0.044 | 0.037 | N/A
 | 10˚C (50 ˚F) | 0.077 | 0.085 | 0.145 | 0.046 | N/A
 | -20˚C (-4 ˚F) | N/A | N/A | N/A | N/A | N/A
Horizontal:
The best performance was achieved at 65˚C (149˚F). Breadboard transported 200 W with 5˚C difference between evaporator and condenser
Operational temperature range:
  At temperatures above the 30˚C (86˚F), breadboard exhibited stable operation
  At 10˚C (50˚F) operation with higher thermal resistance
  At -20˚C (-4˚F) breadboard did not start up
BHM
Worse thermal performance achieved
THM
Breadboard started up only at 50˚C (122 ˚F) when oriented against gravity
Thermal performance in horizontal setup
CHBB_L3_M: large, 14 loops, 2.5 mm internal diameter, methanol
1
2

## Slide 16
Thermal performance
Thermal performance in horizontal setup
Horizontal:
The best performance was achieved at 30˚C (86˚F). Breadboard transported 30 Watts of heat with 3.7˚C difference between evaporator and condenser
Operational temperature range:
  At temperature above the 30˚C (86 ˚F) breadboard exhibited stable operation
  At 10˚C (50˚F) operation with slightly higher thermal resistance
  At -20˚C (-4˚F) breadboard started up, but with high thermal resistance
BHM
Best thermal performance achieved in BHM orientation
THM
Breadboard operated only at higher temperatures (30&45˚C) when oriented against gravity
Thermal resistance ˚C/W |  |  |  |  |  | 
Mode | Orientation | Horizontal |  |  | BHM | THM
 | Heater power | 30W | 20W | 10W | 30W | 30W
Step-up | 45˚C (113˚F) | 0.164 | 0.149 | 0.164 | 0.119 | 0.241
 | 30˚C (86˚F) | 0.124 | 0.124 | 0.148 | 0.123 | 0.332
 | 10˚C (50˚F) | 0.191 | 0.191 | 0.222 | 0.107 | N/A
 | -20˚C (-4˚F) | 1.687 | 1.687 | 2.779 | 0.447 | N/A
CHBB_S3_A: small, 14 loops, 1.5 mm internal diameter, acetone
1
2
3

## Slide 17
Microvib performance
CHBB_L1_M
CHBB_L3_M
CHBB_S3_A
Single spikes reaching up to 250 mN were observed during tests of various breadboards in different orientations
Potential source: thermomechanical stress relaxation or phenomena related to the working fluid, e.g., a vapor burst

## Slide 18
Microvib performance
Series of disturbances observed only in small soldered breadboard, in horizontal and BHM orientation.
Potential source: oscillating fluid motion
Greater and more frequent disturbances were observed during BHM testing, with single force spikes reaching 200–250 mN, while regular oscillations reached up to approximately 100 mN.
A
B
A
B
1
2

## Slide 19
OUR PRODUCTS
SMART MISSION ECOSYSTEM
Summary
MITIGATE

## Slide 20
Outlook
Optimal Filling Ratio: Best performance observed at low filling ratios (15–30%).
Best Small Breadboard: CHBB_S3_M (14 loops, methanol, internal diameter 1.5 mm) achieved 0.123 ˚C/W in nominal conditions.
Best Large Breadboard: CHBB_L3_M (14 loops, methanol, internal diameter 2.5 mm) reached 0.025 ˚C/W in nominal conditions.
Horizontal operation (0-g Operation): All small breadboards operated successfully in the horizontal orientation, whereas among the large breadboards, only the configuration with a larger diameter and methanol demonstrated stable operation at wide condenser temperature range.
Operational temperature range: Most breadboards exhibited improved performance at higher temperatures and power levels; CHBB_S3_A was the only unit to operate at −20 °C (−4 °F), demonstrating the broadest operational temperature range.
Microvibrations: Single spikes, observed across multiple breadboard configurations, may result from either thermomechanical stress relaxation or local vapor burst, whereas series-type disturbances, detected only in the small soldered breadboard, exhibited a repetitive pattern suggestive of fluid oscillations.

## Slide 21
2nd phase of the project
Two final design selected
Test campaign:
  FR tests
  TVAC performance test
  Microvibration tests
  Thermal cycling test
  Vibration testing

## Slide 22
Thank you!
www.kplabs.space
MWOJCIK@KPLABS.PL
KP Labs
Bojkowska 37J
44-100 Gliwice, Poland

## Slide 23
OUR PRODUCTS
SMART MISSION ECOSYSTEM
Backup slides
MITIGATE

## Slide 24
where:
R – thermal resistance [°C/W];
Te – temperature of the evaporator [°C];
Tc – temperature of the condenser [°C];
P – power transported (heat loss included) [W];
Thermal performance
Heat loss test for small bb
Tests conducted in ambient conditions
- Test bench insulated with extruded polystyrene (XPS)
convective heat loss still present
At worst, losses reached up to 30% of total power
Notes: Tutaj wspomnieć, że temperatury do wyliczenia oporu będą wzięte z centrum parowacza skraplacza.
Część czujników przyklejona jest do skraplacza/parowacza bezpośrednio i dają nam one informacje na temat rozkładu temperatury na parowaczu/skraplaczu. (podczas testu na etanolu można było odczytać, że jedna strona PHPa działa lepiej
Pozostałe czujniki przyklejone bezpośrednio do rurek miedzianych, żeby dały informacje

## Slide 25
Test stand
Microvib test
A dynamometer setup: a force plate on four force-links, base plates rigidly mounted on massive concrete foundation.
Noisy environment – test carried out in the night-time
Low signal-to-noise ratio
During microvibration measurements, the coldplate was detached from the condenser via quick couplings
For small breadboard the base plate was suspended to better isolate the setup from external disturbances