## Slide 1: FROSTE: Designing a Thermal Control System for Cryogenic Lunar Sample Return
Elijah Stewart1, Claire Silaire1, Faiyaj Khan2, Greg Schunk3
1NASA MSFC, 2BRC, 3Amentum
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Thermal Control and Protection Technical Session
Presented by: Faiyaj Khan and Claire Silaire

## Slide 2: FROSTE Overview
Frozen Return of Samples to Earth (FROSTE) is targeting cryogenic sample return from Permanently Shadowed Regions (PSRs) at the lunar south pole.
Temperatures at these regions are below 100K and FROSTE will be required to maintain lunar regolith samples at these temperatures through sample collection to splashdown on Earth to preserve the trapped volatiles in the sample.
Stowage Interface (Notional)
Top Lid , MLI
handle
Sample tubes
Core Samples
Tube holder
Phase Change Material (Thermal Mass)
MLI wrap
Outer Casing
MSFC Advanced Concepts Office Preliminary Design
Solar Illumination at the Lunar South Pole[1]

## Slide 3: FROSTE Thermal Challenges
Operate in different environments with varying requirements tied to each. Power availability throughout the mission will require a robust thermal control system. These include:
  Crewed Vehicles
  Lunar Surface
  PSRs
  Transit
  Earth Re-entry
  Sample Recovery
Currently targeting to maintain samples at 80 K. With varying environments above, the thermal control system is using a combination of active and passive thermal management:
  Active
  Stirling cycle cryocooler
  Passive
  Phase Change Material (PCM)
  Multilayer insulation (MLI)
  Thermally isolating structural design
Notes: Challenge: large design space
  Different safety requirements for crewed and non-crewed space
  Sample target temperature is not set which affects overall thermal control architecture
  Robotic vs human interfacing

## Slide 4: FROSTE Thermal Model
PSC x5
SSC
*Lid is hidden
FROSTE Thermal Model
PCM Tank
Structural Supports
iMLI
FROSTE will require three levels of containment for the regolith samples. Currently the thermal model includes the secondary sealed container (SSC), PCM Tank, and primary sealed container (PSC) that will be used to directly contain the samples.
iMLI is modeled using methods developed by Brian Hamill MSFC and presented at TFAWS 2024[2].
PSC design will be defined by the core drilling element. Currently not a part of the FROSTE project and geometry is assumed.
Structural supports are made with S-glass and limit conduction from PCM tank to SSC.
Notes: Materials:
Primary Sealed Container and SSC: Stainless Steel
PCM Tank: Aluminum

## Slide 5: FROSTE Thermal Trade Studies
Thermal Control Architecture
  Passive radiator vs active cryocooler
Cryocooler interface
  Heat exchanger cooling loop with gaseous Neon vs thermal strap
iMLI sizing
PCM tank material selection
  Assessing available additively manufacturable alloys
PCM tank internal design
  Mesh vs fins
PCM cooldown methods
  Finned Lid vs lid removal vs active cooling
Contour plot with thermal strap interface to cryocooler

## Slide 6: FROSTE Heat Loss
Assessed three different thermal environments:
  Cabin environment
  Lunar surface
  PSR
Calculating heat removal required to maintain sample temperatures at 80K
  Cabin is warmest of the three environments
  Lunar surface allows for radiation to deep space
  PSR does not require any heat removal and gets below 80K given enough time out of the sun
Contour plot of SSC on lunar surface

## Slide 7: Phase Change Material
The PCM will be a major constituent of the passive thermal control system
Candidate PCM’s:
  2-Methylpentane (120 K)
  2-Methylbutane (112 K)
Goal: Cool down the PCM as quickly as possible and maintain cryogenic temperatures
Testing currently underway to confirm thermal properties of candidate PCM’s.
PCM Thermal Properties [3]

## Slide 8: PCM Tank Internal Design Trade Study: Finned Structure
Introducing a high conductivity finned structure into the PCM tank assists in heat transfer and overall cooldown
Studies done on different fin thicknesses and materials
Results showed that cooldown time was significantly decreased
  Lunar surface environment
  Originally took 27 days to reach phase change passively
  Finned lid drove phase change to the 7 day mark
Finned Lid Structure to be placed in the PCM Tank
No Lid Cooldown
Finned Lid Cooldown

## Slide 9: Cryocooler Interface Trade Study
Active cooling system consisting of a Ne cooling shroud, Stirling cryocooler, and heat exchanger
Neon cooling loop within the PCM Tank
  Sized to remove up to 15 W of heat leak from the SSC
Stirling Cryocooler:
  Sun Power cryocooler: able to reject 19 W at 100 K
Cryofan rejects heat externally from loop
Heat exchanger:
  Core is made of expanded metal foam within conductive cylinder
  High areal density (25 in2 per 1 in3)
  Metal foam is well within allowable pressure drop for baseline Cryofan capacity
Neon cooling shroud coupled to cryocooler via heat exchanger
Expanded Metal Foam Heat Exchanger
Contour Plot of Heat Exchanger
Cool In
273K
Cool Out
283K

## Slide 10: Volatiles and Pressurization
Unintended loss of cooling can lead to melting and subsequent vaporization of solid volatile(s) in the sample.
  Concerns are rupture of the PSC or leakage through the sealing interface from differential pressure across containers, which may pose crew and mission safety risk
Approach-
  Identify minimum amount of volatile material needed to achieve the substance's vapor pressure at cabin ambient temperature
    6 kg of sample per capsule, 5 capsules per FROSTE device
  Single volatiles[4-5], on the right, are considered independently
    Future verification efforts - JSC's Lunar Crater Observation and Sensing Satellite (LCROSS) data
  Lunar regolith's density[6] & porosity[6] are factored in
Results show that traces amounts of volatiles (percent of sample by mass) need to be present for H20 (5.7e-6%), CO (0.9%), CO2 (2.9%), NH3 (0.2%), C2H4 (1.3%) to reach vapor pressure
  For smaller mass fractions, the risk that enough of the volatile is present in the sample to achieve the pressure is increased
FROSTE SSC Anatomy (Not to Scale)

## Slide 11: Conclusion/Forward Work
Preliminary SSC trade studies have shown reasonable thermal performance and only requiring the use of one cryocooler.
Determined cryocooler could be conductively tied to SSC using thermal strap vs fluid loop.
Additive manufactured proof of concept SSC and perform thermal vacuum testing to verify thermal performance.
Thermal vacuum testing to validate PCM candidates' characteristics.
Provide thermal models for PCM testing and additively manufactured SSC.
Complete Thermal Analysis Report by end of FY25.

## Slide 12
Thank you for your attention!
Questions?

## Slide 13: References
[1] E. Mazarico, G.A. Neumann, D.E. Smith, et al., “Illumination conditions of the lunar polar regions using LOLA topography” (2011). Icarus, 211, pp.1066-1081, Available: https://www.sciencedirect.com/science/article/pii/S0019103510004203?via%3Dihub
[2] B. Hamill, “Development of an Equation to Characterize Heat Flux Through IMLI and A Method to Implement in Thermal Desktop®” (2014). NASA TFAWS, Available: https://ntrs.nasa.gov/citations/20240009584
[3] Yang et al., “A Comprehensive Review on Sub-Zero Temperature Cold Thermal Energy Storage Materials, Technologies and Applications,” Journal of Applied Energy, Vol. 288, 2021.
https://www.sciencedirect.com/science/article/pii/S0306261921001033#f0160
[4] Zhang, Jo Ann, David A. Paige. "Cold-Trapped Organic Compounds at the Poles of the Moon and Mercury: Implications for Origins." Geophysical Research Letters, vol. 36, no. 16, 2009 Available: https://doi.org/10.1029/2009gl038614.
[5] Fray, N., and B. Schmitt. "Sublimation of Ices of Astrophysical Interest: A Bibliographic Review." Planetary and Space Science, vol. 57, no. 14-15, 2009, pp. 2053-2080., Available: https://doi.org/10.1016/j.pss.2009.09.011.
[6] SLS-SPEC-159: Cross Program Design Specifications for Natural Environment Available: https://ntrs.nasa.gov/citations/20210024522
The “PCM Thermal Properties” are from “A comprehensive review on sub-zero temperature cold thermal energy storage materials, technologies, and applications: State of the art and recent developments (https://www.sciencedirect.com/science/article/pii/S0306261921001033).” This reference is licensed under the Creative Commons Attribution-NonCommercial-NoDerivatives 4.0 International License (https://creativecommons.org/licenses/by-nc-nd/4.0/).