## Slide 1: Injector Experiment Simulation and Experiment Design for Centrifugal Nuclear Thermal Rocket Engine
Timothy Blackman, Doctoral Candidate.
Robert A. Frederick, Jr., PhD.
The University of Alabama in Huntsville
Thermal & Fluids Analysis Workshop 2025
NASA Ames Research Center
San Jose, CA
August 4-7, 2025
TFAWS 2025 Thermal Control & Protection Technical Session
Presented by: Timothy Blackman

## Slide 2: Background
Centrifugal Nuclear Thermal Propulsion (CNTP) has been researched since 1954 and is a liquid-core concept of a Nuclear Rocket Engine [1]
Liquid uranium is contained at 5500 K within multiple Centrifugal Fuel Elements (CFEs) [2]
Gaseous hydrogen propellant flows throughout the engine structure keeping temperatures below 800 K
The University of Alabama in Huntsville (UAH) research team has created a 37-core reference configuration which predicts a Specific Impulse of up to 1500 s
Propellant Flow Path [2]
UAH Reference Engine Design [3]

## Slide 3: UAH Experiment Campaign
1D ANTFARM Experiment
Galinstan Experiment

## Slide 4: UAH Bubblina Apparatus
Bubblina Apparatus
Bubblina Experiment Set Up

## Slide 5: UAH BLENDER Apparatus
BLENDER II Apparatus
BLENDER I Apparatus

## Slide 6: Updated BLENDER
BLENDER III Apparatus

## Slide 7: Bubble Dynamics
Bubbles within the CFE are formed via gas injection
Bubble formation can be described through balancing the forces acting on the bubble
Formation can be captured using a high-speed camera
An equivalent bubble size is determined using AI detection and the Ramanujan Ellipse Circumference Approximation
Forces Acting on a Forming Bubble [4]
Bubble Force Balance Equation
Ramanujan Ellipse Circumference Approximation

## Slide 8: Bubble Dynamics
Bubble shape can be predicted using the Reynold’s and Bond (Eӧtӧs) numbers
µl = Liquid Viscosity
ρl = Liquid Density
ρb = Gas Density
σ = Surface Tension
D = Bubble Diameter
g = Gravitational Force
U = Bubble Velocity
Grace Diagram [5]

## Slide 9: Experiment Design
UAH Baseline CFE configuration
  Rotates at 10,000 RPM
  Chamber Pressure = 1450 psi
  Liquid Uranium Layer = 0.34 in
  Pressure Gradient in Layer = 600 psi/in
BLENDER Configuration
  Max Rotation = 4,000 RPM
  Max Chamber Pressure = 500 psi
  Liquid Layer = 1.75 in
Pressure at Injector
Pressure Gradient at Injector

## Slide 10: Experiment Design
Liquids
  Water
  Sodium Polytungstate Solution (SPT-3)
Rotations
  500 RPM
  2000 RPM
  4000 RPM
Injectors
  Number per side: 1-4
  Orifice Diameter: 0.04”
Orifice Sizes
  Upstream: 0.05”
  Downstream: Variable Needle Valve
Chamber Pressures
  0 psi
  250 psi
  500 psi
Chamber Size
  Outside Radius: 2.75 in
  Inside Radius: 1 in
Pressure Gradients
  0.45, 7.18, 28.72 psi/in
  1.35, 21.54, 86.15 psi/in

## Slide 11: Injector Experiment Simulation Using GFSSP
NASA’s Generalized Fluid System Simulation Program (GFSSP) is used to inform the test matrices
Forces modeled on the bubble:
  Pressure
  Drag
  Centrifugal
  Buoyancy
Pipes 58 and 78 model the liquid and bubbles using a FORTRAN subroutine
Assumes one, unchanging bubble with static drag coefficient
Currently, flow is controlled at the injectors
GFSSP Model

## Slide 12: Example SPT3 Test Matrix

## Slide 13: Grace Diagram Testing Box

## Slide 14: Results/Future Work
Data collected from these runs will be used as validation for the CFD engine modelers of the research team
Tangible bubble formation data will be used to improve heat and mass transfer calculations and thus overall engine performance
Bubble data will also be useful for other disciplines that use centrifuges
CFD of ANTFARM [6]
CFE Fission Rate [7]

## Slide 15: Thank You
Timothy Blackman
University of Alabama in Huntsville
timothy.blackman@uah.edu
This work was supported by NASA’s Space Technology Mission Directorate (STMD) through the Space Nuclear Propulsion (SNP) project

## Slide 16: Questions?

## Slide 17: Sources
[1] McCarthy, J., “Nuclear Reactors for Rockets,” 1954.
[2] Houts, M., Patterson, M., Heidet, F., Foster, J., Johns, M., Smith, N., and Allen, J., “Overview of High-Performance Centrifugal Nuclear Thermal Rocket Propulsion System,” presented at the 2020 ANS Virtual Winter Meeting, 2020. https://doi.org/10.13182/T123-33578
[3] Thomas, D., Houts, M., Wang, D., Hollingsworth, K., Frederick, R., and Cassibry, J., “Addressing Challenges to Engineering Feasibility of the Centrifugal Nuclear Thermal Rocket,” International Astronautical Congress, 2024.
[4] Zhang, J., Xia, Z., Huang, L., and Ma, L., “Experimental and Numerical Parametric Studies on Two-Phase Underwater Ramjet,” Journal of Propulsion and Power, Vol. 34, No. 1, 2018, pp. 161–169. https://doi.org/10.2514/1.B36533
[5] Haas, T., Schubert, C., Eickhoff, M., and Pfeifer, H., “A Review of Bubble Dynamics in Liquid Metals,” Metals, Vol. 11, No. 4, 2021, p. 664. https://doi.org/10.3390/met11040664
[6] Ayuthya, P. D. N., and Cassibry, D. J., “Mitigating Liquid Over-Compressibility in Liquid-Gas Models for Centrifugal Nuclear Thermal Propulsion Systems,” presented at the Nuclear and Emerging Technologies for Space 2025, Huntsville, AL, 2025. https://doi.org/doi.org/10.13182/NETS25-47460
[7] Schroll, M., Frederick, R., Thomas, L. D., "Characterization of Engine Cooldown for a Centrifugal Nuclear Thermal Rocket," 75th International Astronautical Congress, Milan, Italy, Oct. 2.024

## Slide 18: Back Up Slides

## Slide 19: FORTRAN Subroutine

## Slide 20: Previous Spinning Experiments
70 psi at 300 RPM (Still)
70 psi at 300 RPM (Burst)

## Slide 21: Motivation for AI-Based Bubble Detection
AI Objective: Improve reliability of bubble detection & tracking under dynamic conditions
Traditional image processing methods struggled with:
  Background variation
  Lighting changes
  Motion blur in spinning mode
Enables accurate measurement of:
  Bubble diameter
  Position
  Velocity

## Slide 22: AI Architecture Overview
Two-Stage Pipeline:
  Mask R-CNN (Detectron2) → generates candidate pixel masks
  CNN Classifier (PyTorch) → confirms if candidate is a bubble
Tracking:
  Kalman filter algorithm for frame-to-frame consistency
Image
Mask R-CNN
CNN Classifier
Kalman
TFAWS 2025 – August 4-7, 2025

## Slide 23: Data Curation Process
Positive Samples:
  Pixel masks labeled using Matlab’s Image Labeler
  Centroids extracted → patches cropped (128×128) to include border reflection
Negative Samples:
  Centroids extracted on blank images → patches cropped (128×128) to include border reflection
  Apply inpainting to known mask regions
  Fill in removed areas using neighboring pixels or Gaussian noise
Mask Generation:
  Binary .png masks saved from segmentation tools
  Converted to COCO JSON using utility scripts
Negative
Positive
CNN Negative and Positive Training Data
TFAWS 2025 – August 4-7, 2025

## Slide 24: App Integration (GUI Tool)
GUI allows user to load:
  Video
  Mask R-CNN model (.pth)
  CNN classifier (.pth)
Performs:
  Mask inference
  CNN filtering
  Kalman filter tracking
Output:
  Tracked .avi videos
  Per-frame CSV and summary velocity CSV
GUI for Still Option
GUI for Spinning Option
TFAWS 2025 – August 4-7, 2025

## Slide 25: Outputs and Visuals
Final Filtered Still Video
TFAWS 2025 – August 4-7, 2025

## Slide 26: Outputs and Visuals
Final Filtered Spinning Video
TFAWS 2025 – August 4-7, 2025